## Slide 1: 3SAQS Network Assessment
Till Stoeckenius, ENVIRON
Three-State Air Quality Working Group
Conference Call
19 December 2013

## Slide 2: Recent Work
Refinement of ozone site database
  Additional state and FLM input
  Identify sites currently expected to be operating 2014 – 2017
  Identify reason for site closures (funding vs logistical or other siting concerns)
  Identify seasonal Forest Service monitors
  Identify sites with co-located NOx
Identify all sites which can be included in 3SAQS
  Currently operating and expected to continue operating
  Potentially being closed primarily due to funding issues

## Slide 3: Recent Work (cont.)
Additional map layers
  Ozone non-attainment areas
  Oil & Gas basin boundaries and total emissions by basin
  Producing wells 2008, 2011, 2011-2008
  RFD areas
Correlation analysis
Potentially underserved areas analysis

## Slide 5
 | WestJump 2008 Emissions (tpy) |  |  |  | 
Basin | NOx | VOC | CO | SOx | PM
D-J | 22,165 | 100,622 | 14,367 | 115 | 717
Piceance | 20,113 | 45,714 | 11,520 | 519 | 1,812
N. San Juan | 5,917 | 2,187 | 6,456 | 30 | 72
Uintah | 15,508 | 97,303 | 11,569 | 431 | 716
Powder River | 20,980 | 14,787 | 15,445 | 596 | 666
Southwest WY | 23,824 | 87,374 | 16,024 | 6,030 | 679
Wind River | 1,335 | 10,993 | 2,062 | 1,276 | 31

## Slide 7
Urban, Pop -Oriented
Industrial
Potential 3SAQS Ozone Monitoring Sites
Other
Co-Located NOx
Seasonal
Potential Closure
Class I Area
O&G NOx
NOx (tpy)

## Slide 8
Potential or Confirmed Site Closure
Wyoming Range
Murphy Ridge
Price
Sunlight Mountain
Kenosha Pass

## Slide 9
Potentially Underserved Area
Thiessen Polygons

## Slide 10
Prevailing Summer Wind Direction

## Slide 11
NOx Point Source > 250 tpy
RFD Area

## Slide 12
Predicted 4th Highest Daily Max 8-hr O3: Apr-Aug 2008 (no fires; 8,000’ Mask)
Predicted 4th Highest Daily Max 8-hr O3: Apr-Aug 2008 (no fires)

## Slide 13
Predicted 4th Highest Daily Max 8-hr O3: Apr-Aug 2008 (no fires; no BC/IC)
Predicted 4th Highest Daily Max 8-hr O3: Apr-Aug 2008 (no fires)

## Slide 14: Inter-Site Correlations

## Slide 16
#5
#4
#3
#2
#1
Ozone Monitor Clusters

## Slide 17
 |  | Colorado National Monument | Palisade Water Treatment | Grand Mesa | Gothic | McClure Pass | Ajax Mountain (will close 2014) | City of Aspen | Silt-Collbran | Sunlight Mountain | Wilson | Flattops #3 | Meeker, CO | Ripple Creek
Cluster | Site / Elev. (m): | 1740 | 1521 | 3040 | 2926 | 2930 | 3415 | 2415 | 2485 | 3224 | 2358 | 2904 | 1994 | 2930
5 | Colorado National Monument | 1 | 0.83346 | 0.76464 | 0.62127 | 0.70457 | 0.65241 | 0.65323 | 0.77756 | 0.74078 | 0.73898 | 0.73661 | 0.72618 | 0.6214
5 | Palisade Water Treatment | 0.83346 | 1 | 0.76271 | 0.51007 | 0.77206 | 0.50355 | 0.61503 | 0.86028 | 0.60676 | 0.82857 | 0.77697 | 0.66545 | 0.74361
5 | Grand Mesa | 0.76464 | 0.76271 | 1 | #N/A | 0.84036 | 0.70732 | 0.54945 | 0.81246 | 0.79435 | 0.7114 | 0.78264 | 0.72909 | 0.81772
2 | Gothic | 0.62127 | 0.51007 | #N/A | 1 | 0.8127 | #N/A | 0.73374 | 0.76168 | 0.71841 | 0.68856 | #N/A | 0.66662 | #N/A
2 | McClure Pass | 0.70457 | 0.77206 | 0.84036 | 0.8127 | 1 | #N/A | 0.73619 | 0.81675 | 0.75888 | 0.78094 | 0.79488 | 0.70792 | #N/A
1 | Ajax Mountain | 0.65241 | 0.50355 | 0.70732 | #N/A | #N/A | 1 | 0.71684 | 0.62201 | 0.83082 | 0.69496 | #N/A | 0.63737 | #N/A
1 | City of Aspen | 0.65323 | 0.61503 | 0.54945 | 0.73374 | 0.73619 | 0.71684 | 1 | 0.73628 | 0.65491 | 0.84122 | #N/A | 0.62741 | #N/A
3 | Silt-Collbran | 0.77756 | 0.86028 | 0.81246 | 0.76168 | 0.81675 | 0.62201 | 0.73628 | 1 | 0.79791 | 0.87304 | 0.82911 | 0.82836 | #N/A
3 | Sunlight Mountain | 0.74078 | 0.60676 | 0.79435 | 0.71841 | 0.75888 | 0.83082 | 0.65491 | 0.79791 | 1 | 0.76147 | 0.82942 | 0.68869 | 0.64728
3 | Wilson | 0.73898 | 0.82857 | 0.7114 | 0.68856 | 0.78094 | 0.69496 | 0.84122 | 0.87304 | 0.76147 | 1 | 0.77122 | 0.80027 | 0.78353
4 | Flattops #3 | 0.73661 | 0.77697 | 0.78264 | #N/A | 0.79488 | #N/A | #N/A | 0.82911 | 0.82942 | 0.77122 | 1 | 0.78576 | 0.83205
4 | Meeker, CO | 0.72618 | 0.66545 | 0.72909 | 0.66662 | 0.70792 | 0.63737 | 0.62741 | 0.82836 | 0.68869 | 0.80027 | 0.78576 | 1 | 0.7959
4 | Ripple Creek | 0.6214 | 0.74361 | 0.81772 | #N/A | #N/A | #N/A | #N/A | #N/A | 0.64728 | 0.78353 | 0.83205 | 0.7959 | 1
Pearson Correlations in Departures from Running 30-Day Mean

## Slide 18: Relationships Between O3 and Altitude
Potential Altitude Effects on O3
  Reduced upwind depositional losses
  Increased potential for stratospheric intrusion impacts
  Reduced impacts from upwind sources located at lower elevations
  Others?
Recent Forest Service Study:
  Highest nighttime O3 at highest elevations
  No correlation of daytime O3 with elevation

## Slide 19: Potentially Underserved Areas
UA6 | 
Pros | Cons
Upwind boundary | No significant sources or population centers
Near Capitol Reef Class I area | High absolute correlations between surrounding sites
 |  |  | Price | Escalante | Canyonlands
 |  | Site ID: | _490071003 | _490170004 | _490370101
 |  | Elevation (m asl): | 1722 | 1789 | 1814
Series | Cor Type | Ozone DV (ppm): | 0.07 | incomplete | 0.068
Anomaly | Pearson | Price | 1 | 0.598 | 0.633
Anomaly | Pearson | Escalante | 0.598 | 1 | 0.752
Anomaly | Pearson | Canyonlands | 0.633 | 0.752 | 1
Absolute | Pearson | Price | 1 | 0.853 | 0.883
Absolute | Pearson | Escalante | 0.853 | 1 | 0.905
Absolute | Pearson | Canyonlands | 0.883 | 0.905 | 1

## Slide 20: Potentially Underserved Areas
UA5 | 
Pros | Cons
Downwind of Uintah Basin | No significant sources or population centers
Cross-border transport | 
Hiawatha RFD on northern edge | 
High values at Rangely and Dinosaur (Lay Peak at much higher elevation) | 

## Slide 21: Potentially Underserved Areas
UA7 | 
Pros | Cons
Near Arches Class I area and Moab | No significant existing sources or major population centers in immediate vicinity
Potential new O&G development (Moab Master Leasing Plan) | 
Only moderate correlations between nearby sites (Canyonlands and Colorado NM) | 
 |  |  | Colorad NM | Canyonlands
 |  | Site ID: | _080771001 | _490370101
 |  | Elevation (m asl): | 1740 | 1814
Time Series | Cor Type | Ozone DV (ppm): | 0.068 | 0.068
Anomaly | Pearson | Colorad NM | 1 | 0.73838
Anomaly | Pearson | Canyonlands | 0.73838 | 1
Absolute | Pearson | Colorad NM | 1 | 0.76543
Absolute | Pearson | Canyonlands | 0.76543 | 1

## Slide 22: Potentially Underserved Areas
UA10 | 
Pros | Cons
Near Black Canyon of the Gunnison NM Class I area | No significant existing sources or major population centers in immediate vicinity
Potential new O&G development (Moab Master Leasing Plan) | Not far from Grand Mesa USFS seasonal site but Grand Mesa is at higher elevation (3040 m)
Some areas of elevated ozone predicted, including areas below 8,000’ | Generally low O3 contribution from anthropogenic sources predicted (WestJump modeling)

## Slide 23: Potentially Underserved Areas
UA1 | 
Pros | Cons
Great Sand Dunes NM on eastern boundary (but at higher elevation) | Isolated; No significant existing sources or major population centers in immediate vicinity
Far from any existing monitoring sites | Far from any emissions sources
Some areas of elevated ozone predicted, including areas below 8,000’ | Generally low O3 contribution from anthropogenic sources predicted (WestJump modeling)

## Slide 24: Next Steps
Step | Deadline
Obtain additional input : | 
NPS review of ozone site metadata | 6 January
RFD shapefiles | 6 January
Comments on potential underserved areas (locations, pros and cons) | 6 January
Prepare draft recommendations memo | 10 January
Discuss recommendations with funding agencies and revise as appropriate | Late January
Document data sources and processing procedures | 31 January