## Slide 1: 3SAQS Network Assessment
Till Stoeckenius, ENVIRON
Three-State Air Quality Working Group
Conference Call
17 January 2014

## Slide 2: What’s New
Reclassified Escalante as “permanent” based on assumed continued BLM funding
Examined CD-C modeling results
Obtained monitoring cost estimates from NPS and UT DAQ (needs refinement)
Developed draft future network configuration scenarios

## Slide 3: CDC Project Impacts on O3 DV (APCA analysis)
Source: CD-C Draft EIS, Fig. 4-40, Nov. 2012 (http://www.blm.gov/pgdata/etc/medialib/blm/wy/information/NEPA/rfodocs/cd_creston.Par.83471.File.dat/AQ-Ch4-FarFieldModel.pdf)

## Slide 4
Sites to Keep | Sites Available to Close | Other Existing Sites | Potential New Sites
(see map) | Walden (end of 2014) Lay Peak (end of 2014) Silt-Collbran Grand Mesa Norwood Trout Creek Pass Dutch John | Hiawatha (potentially closing) Murphy Ridge (potentially closing) Fruitland (potentially closing) Price (potentially closing) Wamsutter VOC (potentially closing) Colorado NM (closing) Sinclair Casper (industry) | Douglas Pass Kremmling Rawlins North Riverton Paradox
Can assume all these sites are expected to continue operating thru 2017 without any additional 3SAQS funding?

## Slide 5
Site Reference Map with UAs

## Slide 6
Site Reference Map with O&G NOx Emissions

## Slide 7: Construction of Future Network Configuration Scenarios
Start with existing network as base case
List potential network changes
  Open a new site (no associated site closure)
  Move existing site to new location
  Close existing site
Identify alternative 2014 - 2017 configuration scenarios
  Each scenario consists of one or more site changes (new, move, and/or close)
  Rank order scenarios based on degree to which objectives achieved
  Estimate project funding needed for each scenario

## Slide 8: Base Case Network Configuration
Site | Proposed 2014-17 Status | Base Case Assumptions
Six Sites funded (directly/indirectly) by 3-State Pilot Study (2011/12 through mid-2014) : |  | 
Wamsutter VOC | close or keep in some form? | ??
Lay Peak | keep through 2014, then move to Dinosaur East | Fund site move and 2015-2017 operation
Walden | Keep | Continued funding by??
Escalante | Keep | Continued BLM funding (sufficient?)
Fruitland | Keep | Fund UT DAQ operations via 3SAQS
Price | Keep | Fund UT DAQ operations via 3SAQS
All other sites not scheduled to close: |  | 
(see map; note that Murphy Ridge and/or Hiawatha may close in 2014) | Keep | Funded and operated through existing arrangements (not part of 3SAQS budget)
Which of these sites will the states/agencies not be able to operate 2014-2017 without additional 3SAQS funding?

## Slide 9: Base Case Network (Note: Murphy Ridge and/or Hiawatha may close in 2014)
Which sites will the states/agencies not be able to fund 2014-2017 without additional project funds?

## Slide 10: Potential Actions Beyond Base Case
Potential Action | Primary Supported Objective(s) | Available Cost Offsets | Priority /ID | Cost Impact w/ Offset
Establish new site at Douglas Pass (USFS) | UA13-Roan Plateau (source impact monitoring; cross-border transport) | Close (USFS) Silt-Collbran | H1 | Site move
Establish new site at East Dinosaur early 2014 (CDPHE) | UA5-Dinosaur East (source impact monitoring; cross-border transport) | Close (CDPHE) Lay Peak in late 2014 | H2 | Site move Operating E. Dinosaur for 1 year
Establish new site near Kremmling (USFS) | UA12-Kremmling Area (C1 area monitoring and MPE) | Close (USFS) Trout Creek Pass | H3 | Site move
Maintain Fruitland site | Background monitoring |  | H4 | Operate existing site
Maintain Price site | Source impact monitoring and MPE |  | H5 | Operate existing site
Maintain Hiawatha site | Source impact monitoring |  | H6 | Potential contribution to operation of existing site
Establish fixed site at end of mobile trailer monitoring period | Continued source impact monitoring in UA2 East-Central WY |  | H7 | None if WY can fund
Establish new USFS Rawlins North site | UA3-Medicine Bow – Saratoga (CDC new development impact; MPE) | Close Grand Mesa or Dutch John (or both?) | H8 | Site move
Establish new WYDEQ site near Riverton | UA4-Central West WY (MPE) |  | M1 | New site
Establish new USFS site near Paradox | UA9-Dove Creek North (potential new development; MPE) | Close Norwood (USFS) | M2 | Site move
MPE = Model Performance Evaluation

## Slide 11: Flexibility
States don’t have make monitors at sites permanent, can be Special Purpose indefinitely
State can decide to close or move sites during the 14-17 timeframe, but consult with 3SAQS cooperators first

## Slide 12: Monitoring Cost Elements
Item | $ | Comments
Equipment acquisition (including shelter) | $ per site | Can existing equipment be used?
Equipment depreciation | $ per site | Will this get charged to 3SAQS project?
New site installation (including site scouting trip, equipment delivery, setup and testing) | $ per site | Every site is different and costs will vary depending on state/agency; just need generic estimates for now
On-Site operations (land lease, data link, other utilities, site visits, QC ops, audits) | $ per year | 
Off-Site operations (data handling, QA and reporting) | $ per year | 
Site decommissioning | $ per site | Do not include in 3SAQS budget discussions?

## Slide 13: Cost Allocation
Which cost elements will require 3SAQS funding?
  Varies depending on specific network change being considered
Who has capacity, how much can do without needing more resources? What additional $$ is needed?

## Slide 14: Preliminary Cost and Budget Estimates
There is currently a placeholder in the budget for FY2015-2017 monitoring operations of $450k.
Operations
  NPS: Average per site cost per year of paying a contractor to poll, QA, and report the data it is approximately $28,580 - $37,000 ($85.7 – $111k for 3 years) Is this just for off-site operations?
  UT DAQ: Cost for on and off site operations is $25k - $30k per site-year (specific to Fruitland and Price)
NPS: One site move to new location costs $20k - $50k absent any in-kind contribution by participating agency

## Slide 15: Recommended Network Configuration Scenarios (2014 – 2017) (DRAFT)
Scenario (Potential Actions) | New Sites | Maintain Sites (plus all “permanent” sites) | Project Costs and Required Offsets and In-Kind Contributions
S0 (Base Case) (lowest cost) | Replace Lay Peak with Dinosaur E. end of 2014 | All operating sites including Fruitland, Price, Escalante, Walden, Lay Peak (thru 2014), Wamsutter VOC?? | -Support for UT DAQ operation of Fruitland and Price -Establish and operate Dinosaur E. starting 2015 as replacement for Lay Peak -All other sites as currently funded
S1 (H4, H5, H6, H1) (medium cost) | Douglas Pass (USFS) Dinosaur E. (replaces Lay Peaak end of 2014) | As in Base Case plus Hiawatha (assuming WYDEQ needs funding) | -3SAQS funds Fruitland, Price, Hiawatha -Closure of Silt-Collbran; -USFS operates new Douglas Pass site
S2 (H4, H5, H1, H2, H3) (medium cost) | Douglas Pass (USFS) Dinosaur East Kremmling | As in Base Case | -Closure of Silt-Collbran, Trout Creek Pass and (at end of 2014) Lay Peak; -USFS operates new Douglas Pass and and Kremmling sites (no net change in operating costs) -Dinosaur East site 2015-2017 operation costs offset by Lay Peak closure -WYDEQ maintains Hiawatha
S3 (H4, H5, H1, H2, H3, H8) (highest cost) | Douglas Pass Dinosaur East Kremmling Rawlins North | As in Base Case | -Closure of Silt-Collbran and Trout Creek Pass -Closure of Lay Peak (end of 2014) -USFS operates new Douglas Pass and Kremmling sites (no net change in operating cost) -Dinosaur East site 2015-2017 operation costs offset by Lay Peak closure -WYDEQ maintains Hiawatha

## Slide 16: Scenario 1
Additional Assumptions:
-Murphy Ridge closes

## Slide 17: Next Steps – Jan. 24th through mid-Feb.
Step | Deadline
Obtain additional input : | 
Call for Assessment WG to reach consensus on draft recommendations | TODAY!!
States/agencies provide additional information on: Monitoring cost element estimates Available in-kind contributions | 24 – 31 January
Additional calls as needed for Assessment WG to reach consensus | Possible calls on 28 and/or 29 January, or morning of 31 January
Complete recommendations presentation for distribution to Steering Committee | before or on 6 February
Review of recommendations by Steering Committee, including input on site operations commitments by each funding agency | by 14 February
Finalize recommendations including data files, map layers, data sources and processing procedures | 21 February