## Slide 1: Department of Environmental Quality
March 22, 2018
Emissions Projection Methods for Agriculture and Construction Diesel Nonroad Mobile Emissions Categories

## Slide 2: NONROAD Model Growth Factor Refinements
Default NONROAD Model Growth Data
  Growth Indices (1996 = 1000) by FIPS, Indicator Code (sector/fuel type), and Year
  Model Values Generally Reflect Growth Rates Calculated from Estimated National Engine Populations by Sector/Fuel Type in 1989 and 1996
  Limitations
    Growth rates from early 1990s continue for all post-1996 years
    National growth rates apply to all geographic areas
North Carolina Division of Air Quality (NC DAQ) Prioritization
  Construction and Agriculture Sector Diesel Equipment
    Greater than half of total NONROAD Model 2011 NOx emissions in NC
Department of Environmental Quality

## Slide 3: NONROAD Model Growth Factor Refinements
NONROAD Default Growth Indices
  Model Interpolates Values for Missing Years
Department of Environmental Quality
Year | Construction Sector Diesel | Agriculture Sector Diesel
1996 | 1000 | 1000
1998 | 1063 | 1063
2000 | 1125 | 1126
2005 | 1286 | 1271
2010 | 1446 | 1414
2015 | 1607 | 1558
2025 | 1927 | 1845
2045 | 2569 | 2420

## Slide 4: NONROAD Model Growth Factor Refinements
U.S. Energy Information Administration (EIA) No. 2 Diesel Sales/Deliveries for North Carolina (1000 gallons)
1 U.S. EIA, “North Carolina No 2 Diesel Off-Highway Construction,” accessed from http://www.eia.gov/dnav/pet/hist/LeafHandler.ashx?n=PET&s=K2DVCNSNC1&f=A
2 U.S. EIA, “North Carolina No 2 Diesel Sales/Deliveries to Farm Consumers,” accessed from http://www.eia.gov/dnav/pet/hist/LeafHandler.ashx?n=PET&s=K2DVFMSNC1&f=A
Department of Environmental Quality
Year | Off-Highway Construction1 | Farm Consumers2
1996 | 56,304 | 30,029
2000 | 45,600 | 36,850
2005 | 39,846 | 29,776
2010 | 43,175 | 38,594
2015 | 41,130 | 44,834

## Slide 5: NONROAD Model Growth Factor Refinements
Department of Environmental Quality
Replace National Default Growth Rates
  Incorporate NC-specific records (apply default NONROAD growth rates for post-2015 years)
Year | Construction Sector Diesel |  | Agriculture Sector Diesel | 
 | NONROAD Default (FIPS 00000) | North Carolina (FIPS 37000) | NONROAD Default (FIPS 00000) | North Carolina (FIPS 37000)
1996 | 1000 | 1000 | 1000 | 1000
2000 | 1125 | 810 | 1126 | 1227
2005 | 1286 | 708 | 1271 | 992
2010 | 1446 | 767 | 1414 | 1285
2015 | 1607 | 730 | 1558 | 1493
2025 | 1927 | 876 | 1845 | 1765
2045 | 2569 | 1168 | 2420 | 2319

## Slide 6: NONROAD Model Growth Factor Refinements
Growth Rate Comparisons
  NONROAD National Defaults versus EIA Fuel Sales-Based Values
Method Incorporated into Version 2 of the 2014 NEI
Department of Environmental Quality
Years | Agriculture Sector Diesel |  | Construction Sector Diesel | 
 | Default | NC DAQ | Default | NC DAQ
1996-2015 | +56% | +49% | +61% | -27%
1996-2025 | +85% | +77% | +93% | -12%
1996-2045 | +142% | +132% | +157% | +17%

## Slide 7: NONROAD Model Growth Factor Refinements
Contact Info:
  Andy Bollman, NC Division of Air Quality
  andrew.bollman@ncdenr.gov
  919-707-8499
Department of Environmental Quality