## Slide 1: GEOS-Chem 2017 Modeling
Task Summary
Ou Nopmongcol, Jean Guo, Yuge Shi, Chris Emery
December 14, 2021

## Slide 2: Background
UDAQ is modeling 2017 for SIPs and needed boundary conditions for CAMx
WESTAR was also planning for 2017 WAQS
Two GEOS-Chem simulations
  2017 Base Case
  2017 Scenario with non-US anthropogenic emissions set to zero (Zero Rest of World run; ZROW)

## Slide 3: Project Schedule
Task | Anticipated Completion | Note
Simulations completed | End of Feb | Completed
GEOS-Chem output to UDAQ | March 4 | Completed
Model Performance Evaluation | March 26 | Completed
Final Report | April 9 | Completed
Notes: Did UDAQ have any issue with BC extraction?

## Slide 4: Emission inputs

## Slide 5: Global Modeling
Global anthropogenic emissions based on latest global and regional inventories available for GEOS-Chem
  Region-specific :
    US NEI 2011
    Canada CAC 2014
    China MEIC 2017
  Global:
    Anthropogenic: Community Emission Data System (CEDS)
    Biomass burning: Global Fire Emissions Dataset (GFED)
    Natural sources driven by 2017 meteorology (biogenic/soil, oceanic, dust, LNOx)
Notes: soil NOx, sea-salt, oceanic DMS, biogenic VOC, WBD, short-lived bromo-carbon

## Slide 6: GEOS-Chem Configuration Comparison

## Slide 7: Emissions used in the 2017 GEOS-Chem

## Slide 8: Emission Scalers
CEDS 2014->2017 scalers range 0.88-1.06

## Slide 9: Emission Scalers
Notes: C2H6 from oil and gas and biofuel

## Slide 10: ZROW Simulation
Mask applied to global EIs
Notes: Global methane is important in the ZROW scenario. GEOS-Chem specifies methane by interpolating global measurements rather than computing methane from emissions and chemistry (as for VOC). Any change we make to the measurements will be somewhat arbitrary. We propose that the effects of methane be addressed as weight-of-evidence. For example, Butler et al., 2020 suggests 1 ppb ozone decreases in northern hemisphere average surface ozone when methane is reduced by ~20%.

## Slide 11: Post-processing
Spatial Plots of quarterly average concentrations across North America
CAMx boundary conditions
  New output species to be mapped to CAMx model species
  CAMx meteorological files from UDAQ for testing and QA
Model Performance Evaluation
  Ozone (CASTNET) and PM2.5 (IMPROVE)
    Spatial maps of NMB/NME, Summary table
  Ozonesonde at Trinidad Head (CA) and Boulder (CO)

## Slide 12: Quarterly spatial plots

## Slide 13
Q1
ZROW - Base
Base
ZROW
Q2
Base
ZROW
ZROW - Base
MDA8 Ozone

## Slide 14
Q3
ZROW - Base
Base
ZROW
Q4
Base
ZROW
ZROW - Base
MDA8 Ozone

## Slide 15
Base
ZROW
Q1
ZROW - Base
ZROW - Base
Base
ZROW
Q2
Average PM2.5

## Slide 16
Base
ZROW
Q3
ZROW - Base
ZROW - Base
Base
ZROW
Q4
Average PM2.5
Notes: Typical hot spots as seen in 2014 as well. Fire impacts in Canada seem high, although they are localized.
Overall, similar spatial patterns but lower magnitude compared to the 2014 results

## Slide 17: Fire-driven PM2.5 peaks
Mexico in Q2
Canada in Q3
Notes: OCPI = Hydrophilic organic carbon aerosol
OCPO = Hydrophobic organic carbon aerosol

## Slide 18: Model Performance Evaluation

## Slide 19: Ozone CASTNET Summer, All Western Sites
Biases below <±15% criteria except in May
Slight tendency to underestimate
Correlation of 0.56 – 0.68
Period | NMB (%) | NME (%) | Correlation (r)
May | -19.3 | 19.6 | 0.68
June | -11.5 | 14.3 | 0.67
July | -1.1 | 12.1 | 0.49
August | 4.1 | 10.6 | 0.56
Performance Criteria: Bias <±15%, Error < 25%, r > 0.5
Hourly ozone Q-Q plot
MDA8 Ozone
Notes: Model performance evaluation focusing rural sites
Bias = Normalized Mean Bias
Error = Normalized Mean Error

## Slide 20: Ozone NMB (%)
Tends to underestimate ozone
Largest biases in California in over all four months (Pinnacle and Sequoia) and the Rocky Mountain states in May
May
Jun
Jul
Aug

## Slide 21: PM2.5 IMPROVE 4 Quarters, All Western Sites
Better performance in Q2/Q4 than Q1/Q3
Over prediction of NO3 in colder months
Tendency to over-estimate in the southwest due to overstated dust
Period | NMB (%) | NME (%) | Correlation (r)
Q1 | 68 | 104 | 0.21
Q2 | 3.8 | 48 | 0.25
Q3 | 8.8 | 51 | 0.49
Q4 | 38 | 91 | 0.24
Performance Criteria: Bias <±30%, Error < 50%, r > 0.4
24-hr avg PM2.5
Notes: Consistent over prediction of sulfate, nitrate drives poor performance in Q1 and Q4
Consistent under prediction of organics
Other PM2.5 high throughout the year with highest biases in Q2 in the southwestern US attributable to overstated dust emissions

## Slide 22: Ozone sonde comparison: Boulder
Tendency to underestimate below 5 km in May and June
Good performance aloft in all months
May June
July August
May-Aug

## Slide 23: Ozone sonde comparison: Trinidad Head
Tendency to underestimate below 10 km in May and June
Generally good performance aloft
  Slight overestimation in August
May June
July August
May-Aug
Notes: Trinidad Head
May – 6 days
June – 3 days
July – 5 days
Aug – 3 days

## Slide 24: Testing CAMx BC extraction

## Slide 25: Test Case Using UDAQ’s CAMx 12km meteorological file for June 1
Qualitative evaluation for QA
General agreement in patterns suggests a proper spatial extraction
GEOS-Chem output
CAMx BCs
Notes: Curtain plot of the Western BCs
GEOS-Chem and CAMx employ different vertical and horizontal coordinate systems, so the visual comparison suggests differences by the way they are plotted

## Slide 26: Summary
GEOS-Chem 2017 modeling setup seems reasonable
  Base case shows reasonable ozone performance
  PM2.5 performance not as good, particularly in colder seasons
    Much less likely driven by global transport than by local processes
Recommend that the effects of methane (not assessed in the ZROW simulation) be addressed as weight-of-evidence in the 179B demonstration
Developed 2017 CAMx IC/BC for WAQS
Notes: Effects of methane were not assessed in the ZROW simulation due to the limitation of how global methane is treated in the GEOS-Chem model. We recommend that the effects of methane be addressed as weight-of-evidence in the 179B demonstration

## Slide 27: Questions? cemery@ramboll.com Chris Emery Senior Managing Consultant