## Slide 1: WRAP 2014 Shake-Out Study
Phase III Progress Update
And Phase IV Plans
2014v2 Actual Base Case, Representative Baseline & 2028 Modeling and Dynamic Evaluation
Ramboll US Corporation and UNC Chapel Hill
Regional Haze Planning Work Group
October 31, 2019

## Slide 2: WRAP 2014 Shake-Out Study Phase I & II
Phase I and II conducted from Dec 2018 through May 2019
  Developed CAMx & CMAQ 2014v1 36/12-km Shake-Out Study modeling platform
    http://views.cira.colostate.edu/iwdw/docs/waqs_2014v1_shakeout_study.aspx
  Performance issues found that were addressed in Phase III Modeling:
    EPA’s 2014 GEOS-Chem simulation overestimated ozone
    Coastal SO4 overestimation in CAMx
    NO3 underestimation
    BEIS vs MEGAN biogenic emissions

## Slide 3: 2014v1 Shake-out final configuration
CAMx v6.5 and CMAQ v5.2.1 (April 2018 releases)
WAQS WRF Meteorology -- 36US and 12-km 12WUS2 domains (one-way grid nesting)
  Better precipitation than EPA 12-km 12US2
25 vertical layers (collapse from WRF 36 layers)
WRAP Shake-Out 2014v1 emissions
  2014NEIv2 with western state updates for Point/Non-Point
BEIS biogenic emissions
  Better OA model performance than MEGAN v3.0
  Some MPE issues in final 2014v1 annual runs
Boundary Conditions based on EPA’s 2014 GEOS-Chem simulation with corrected volcano emissions for Jun/Jul3
  EPA GCBCs produced overstated ozone

## Slide 4: Current Phase III 2014 Shake-Out Tasks (Oct 31, 2019)
Task | Description
1.1 | 2014v1 Additional PGM Sensitivity Tests
1.2 | Revised 2014 GEOS-Chem Modeling
1.3 | 2014v2 Emissions Modeling Updates
1.4 | Fire Plume Rise Sensitivity Modeling
1.5 | Additional PGM Sensitivity Tests
1.6 | Annual CMAQ/CAMx 2014v2 Shake-Out MPE
1.7 | 2014 GEOS-Chem/PGM NAT and ZROW
1.8 | Anthropogenic/Natural PM Source Apportionment
2.1 | Representative Baseline EGU Profiles
2.2 | Rep. Baseline SMOKE fire, O&G and EGUs
2.3 | Rep. Baseline PGM Modeling
3.1 | Dynamic Model Evaluation Scoping Study
5.1 | Management for Phase III Shake-Out Study
Completed Partially Completed
Discussed on Sep 10 RTOWG Call
Reduce Scope
Eliminate Task
Initial CAMx 2014v2a
GEOS-Chem Part Done
Completed
Completed
Ongoing
Ongoing

## Slide 5: Content: WRAP 2014 Shake-Out Oct 31, 2019 Update
Phase I & II Tasks 1.1 (2014v1 Sens), 1.2 (2014 GEOS-Chem) and 1.3 (2014v2 EI)
Reduction in Scope for Tasks 1.4 (Fire Plume Rise) and 1.5 (Additional Sens)
Initial CAMx 2014v2a 36/12-km under Task 1.6 (Annual 2014v2 Shake-Out Runs)
Re-mapping of emissions to take advantage of new CAMx v7.0
  Highlights from EPA’s national regional haze modeling released Sep 19, 2019
  Advantages of explicit treatment of elements in CAMx v7.0
Next Steps for WRAP 2014 Shake-Out Phase III 2014v2 Base Case and Representative Baseline modeling
Path Forward for WRAP 2014 Shake-out Phase IV:
  Dynamic Evaluation
  2028 Modeling
  Model Verification on IWDW Servers

## Slide 6: Task 1.1: Preliminary 2014v1 PGM Sensitivity Tests
Objective: Investigate model performance and other issues that can be performed using the 2014v1 platform before revised 2014 GEOS-Chem and 2014v2 emissions are available
  Coastal SO4 Overestimation; Bi-Directional (BiDi) Ammonia Deposition; New Version of CAMx (v7.0) and CMAQ (v5.3)
  New CAMx 2014v2 Model Configuration (vs. 2014v1 Configuration):
    CAMx v7.0 (vs. CAMx v6.5)
    Explicit DMS Chemistry (vs. rename DMS as SO2)
    BEIS Biogenic Emissions (vs. MEGAN v3.1 not ready in time)
  New CMAQ Version:
    CMAQ v5.3 (released Aug 27, 2019)

## Slide 7: Task 1.2: Revised 2014 GEOS-Chem Simulation
Objective: Conduct 2014 GEOS-Chem using approach used in recent 2016 GEOS-Chem to generate new PGM 36-km GCBCs and perform Jan/Jul PGM sensitivity tests to evaluate new GCBCs that will hopefully reduce ozone overestimation bias.
  2014 GEOS-Chem Simulation; CAMx BC-only inert; CAMx Jan/Jul GCBC Photochemistry
    Corrected systematic ozone overestimation bias from EPA’s 2014 GEOS-Chem run
BC-Only Annual Inert CAMx Simulation
Lava Beds (N-CA)
Canyonlands (SE-UT)
EPA 2014 GEOS-Chem
WRAP 2014 GEOS-Chem
N-CA
SE-UT

## Slide 8: Task 1.3: 2014v2 SMOKE Emissions Modeling
Objective: Develop 2014v2 36/12-km emission inputs using SMOKE: all new California emissions (requires processing of all other states too); minor updates to other states; new 2014v2 O&G emissions for WRAP states
  Reasonable agreement with 2014NEIv2 and 2014 CARB On-Road Mobile Emissions (< ±10%)
  Reasonable agreement with total other source emissions, except for Ammonia with 2014NEIv2 73% higher than CARB 2014

## Slide 9: Task 1.4: Fire Plume Rise Sensitivity
Objective: To evaluate WRAP vs. SMOKE-Briggs plume rise approaches for processing fires for input into CAMx (Reduced Scope).
  SMOKE-Briggs plume rise processing approach takes weeks to generate 3-D files of emissions (6 Tb) that need to be turned into thousands of virtual point sources for modeling in CAMx
  Compare CAMx 2014 Q3 MPE using WRAP vs. SMOKE-Briggs Plume Rise:
    Comparable model performance (EC and OA)
    WRAP plume rise higher primary near source, Briggs more widespread fire impacts
  Tentatively select WRAP plume rise due to more efficient and comparable MPE
Task 1.5: Additional Sensitivity Modeling Using 2014v2
Objective: Evaluate MEGAN v3.1 and other sensitivities that need corrected 2014 GEOS-Chem BCs.
    Cancel task and re-assign resources toward 2028 modeling

## Slide 10: Task 1.6: CAMx/CMAQ 2014v2 Base Case Modeling
Objective: To conduct CAMx and CMAQ annual 36/12-km simulations and model performance evaluation (MPE) using the new 2014v2 modeling platform
  Merged Task 1.3 2014v2 emission updates (e.g., California and WRAP O&G) with 2014v1 emissions.
  Conduct CAMx v7.0 annual 2014v2a 36/12-km simulation and initial MPE
    High January modeled ozone concentrations in northeast Wyoming
    O&G temporal profile from EPA 2014 platform for some counties (e.g., Weston County, WY in PRB) allocated all annual emissions to just January producing high VOC/NOx emissions
    Need to re-SMOKE 2014v2 O&G emissions
  Given this delay to re-SMOKE 2014v2 O&G, we decided to re-map the 2014v1 and 2014v2 emissions to take advantage of the new element species (Al, Si, Ca, Fe and Ti) in CAM v7.0
    No new SMOKE modeling, re-running of CMAQ2CAMx emissions processor w/ new species mappings
    Also pick up CMAQ SOAALK SOA precursor species that is currently dropped by CMAQ2CAMx emissions processor

## Slide 11: Epa 2016 National Regional Haze modeling using camx v7.0
EPA 2016 national regional haze modeling results released September 19, 2016
  2016 national reginal haze modeling included 2016 base case with MPE and 2028 visibility projections with sector only (no geographic regions) breakdown source apportionment
Advantages to using explicit treatment of elements in CAMx v7.0:
  Treatment of Calcium Nitrate [i.e., Ca(NO3)2] that could be important in arid western U.S., especially in the summer because it is non-volatile unlike Ammonium Nitrate that evaporates when hot
  Metals (Fe) treatment in aqueous-phase Sulfate formation
  Mapping to IMPROVE Soil species [instead of using other PM2.5 (FPRM + FCRS)] for current IMPROVE light extinction equation:

## Slide 12: Example EPA 2016 Model performance by Region
In WRAP region, mainly Sulfate overestimation and Nitrate underestimation tendency
  In EUSA, Sulfate lower bias (<±20%) to slight overestimation
  In EUSA, Nitrate overestimation bias. Explains different settings for Ammonia deposition in EPA 2016 beta’ and WRAP 2014v2:
    EPA 2016 beta’: No BiDi & Rscale = 0 (no surface resistance)
    WRAP 204v2: w/ BiDi and Rscale = 1 (w/ surface resistance)
SO4
NO3
Goal <±10%
Criteria <±30%
Goal <±15%
Criteria <±65%

## Slide 13: EXAMPLE EPA 2016/2028 beta’ glideslopes (CAMx v7.0)

## Slide 14: Path forward with WRAP 2014v2 modeling (Task 1.6)
Focus on CAMx v7.0 and try to finish first 2028 simulation by end of 2019
  Add CMAQ v5.3 as time permits not interfering with primary goal for 2028 modeling
Updates to initial CAMx 2014v2a simulation for 2014v2b (Complete: Oct 23, 2019):
  SMOKE re-processing of WRAP 2014v2 O&G emissions correcting EPA 2014 platform O&G temporal profiles
  Rerun CMAQ2CAMx processor of 2014v1/2014v2 CMAQ-ready emissions for CAMx:
    Explicit treatment of element species (Al, Si, Ca, Fe and Ti)
    Mapping of SOAALK to CAMx SOA-precursor species (IVOA) [Not used in EPA 2016 beta’]
    Although no new SMOKE modeling, CMAQ2CAMx cycles through many Tb of data
  Testing of WRAP vs. SMOKE Briggs fire plume rise approach (Complete: Oct 20, 2019)
    WRAP plume rise approach much more efficient in CAMx (Ptop/Pbot)
    Selected WRAP for 2014v2b as comparable MPE
  Delays in completing tasks due to power outage in Novato CA Oct 26-29

## Slide 15: Status of remainder phase III Shake-Out Tasks (1 OF 2)
Task 1.7: Natural and ZROW Modeling -- STARTED
  Objective: Conduct linked 2014 GEOS-Chem and PGM 36/12-km modeling for a Natural (no anthropogenic emissions) and ZROW (no international anthro emissions – Zero-Out Rest of World).
    2014 GEOS-Chem Natural Simulation -- DONE
    2014 36/12-km PGM Natural Simulation – WAITING FOR CAMX 2014V2 RepBase RUN
    2014 GEOS-Chem ZROW Simulation – DONE
    2014 36/12-km PGM ZROW Simulation -- WAITING FOR CAMX 2014V2 RepBase RUN
Task 1.8: Broad-Based Anthro vs. Natural PM Source Apportionment – NOT STARTED
  Objective: Conduct CAMx 2014v2 RepBase 36/12-km PSAT Source Apportionment modeling separating contributions of natural and anthropogenic emissions.
    CAMx 2014v2 36/12-km two-way PSAT using 2014 GCBC and 2014 Natural GCBCs and separate tracking of U.S. and non-U.S. anthropogenic emissions.
    Post-processing of and PPT on PSAT results.
Task 2.1: Representative Baseline EGU Emissions and Temporal Profiles -- DONE
  Objective: Develop plan for adding other emissions (i.e., PM, CO, NH3 and VOC) to current Representative Baseline and 2028 future year EGU emissions.
    Draft and Final EGU Representative Baseline plan.

## Slide 16: Status of remainder phase III Shake-Out Tasks (2 OF 2)
Task 2.2: Representative Baseline (RepBase) Emissions Modeling – ONGOING
  Objective: SMOKE emissions modeling of Representative Baseline EGU, O&G and Fire emissions.
    SMOKE emissions modeling of Representative Baseline and 2028 EGU emissions.
    SMOKE emissions modeling of Representative Baseline O&G emissions.
    SMOKE emissions modeling of Representative Baseline Fire emissions.
    PPT on Representative Baseline emissions modeling.
Task 2.3: Representative Baseline (RepBase) PGM Modeling – NOT STARTED
  Objective: Current representative Baseline CAMx and CMAQ modeling using 2014v2 platform.
    CAMx 36/12-km 2014v2 Representative Baseline modeling.
    CMAQ 36/12-km 2014v2 Representative Baseline modeling.
    PPT on Representative Baseline PGM modeling.
Task 3.1: Dynamic Evaluation Scoping –COMPLETED
  Objective: Develop plan for conducting 2002 to 2014 dynamic model evaluation using database. 2014v2 RepBase
    Draft plan for conducting dynamic evaluation – DRAFT PLAN DISCUSED WITH RTOWG CO-CHAIRS
    Final plan for conducting dynamic evaluation – IN PROCESS OF UPDATING FINAL PLAN

## Slide 17: Wrap 2014 Shake-Out study Phase IV Work Effort
Task 4: Conduct Dynamic Evaluation
  Backcast 2014 anthropogenic emissions to 2002
  Hold natural emissions and Boundary Conditions constant at 2014v2 RepBase levels
  CAMx 2002 modeling and dynamic evaluation:
    Compare observed 2000-2004 to 2014-2018 vs. modeled 2002 to RepBase visibility changes
Task 5: 2028 OTB/OTW Modeling
  2028 Emissions development and processing
  2028 CAMx modeling and 2028 visibility projections
    CMAQ v5.3 modeling as time permits
  Transfer of results and ability to generate graphical displays to IWDW (e.g., TSS2)
Task 6: WRAP 2014v2 Platform Verification on IWDW Servers
  Reproduce WRAP PGM Modeling 2014v2 Base, RepBase and 2028 modeling on IWDW computers
  Assist and support IWDW in developing regional haze SIP products

## Slide 18: Representative Baseline (RB) and 2028 emissions
Modeled Representative Baseline (RepBase) and 2028 results are used in a relative fashion to scale observed 2014-2018 baseline visibility (PM) to obtain 2028 visibility impairment
  Relative Response Factors: RRF = Model2028 / ModelRepBase
  Visibility2028 = Visibility2014-2018 X RRF
  Therefore, important that RepBase and 2028 emissions are consistent with each other
EPA guidance for projecting future year visibility impairment recommends using modeled results from base year (2014) for IMPROVE Most Impaired Days (MID) for the RRFs to scale the observed IMPROVE MID from the 2014-2018 Baseline to 2028
  RepBase uses different fire emissions than 2014 actual, so using observed 2014 IMPROVE MID for RRFs may be inappropriate
  Need to investigate alternative approaches to RRFs, such as RepBase modeled MID
Following slides focus on the available emissions for the RB and 2028 emissions and our recommendations for use in the two emission inventories

## Slide 19: Sources of Rep Baseline (RB) and 2028 emissions
WRAP-2014v2 – Actual 2014v2 (used for RB & 2028 Natural: Bio, LNOx, SSA/DMS, WBD)
EPA-2028v1 & EPA-2016v1 – EPA’s 2016v2 platform emissions (Nov 2019?)
CARB-2028 & CARB-2014v2 – CARBs emissions for California
WRAP-2028-EGU & WRAP-RB-EGU – WRAP EGU Emissions Analysis Project (CNEE)
WRAP-2028-O&G & WRAP-RB-O&G – WRAP OGWG RB & 2028 O&G Emissions Study
WRAP-2028-Mobile – 2028 On-Road/Non-Road Emission Inputs for 12WUS2 domain
WRAP-RB-Fires – WRAP FSWG developing RB fires for both RB & 2028 OTB/OTW scenarios
For 36-km 36US domain aggregate 12-km 12WUS2 domain emissions to 36-km and replace 36-km emissions at location of 12WUS2 domain

## Slide 20: Source of RB and 2028 emissions by Source Category
Source Sector | Representative Baseline | 2028 OTB | 2028 SMOKE Required
California All Sectors 12WUS2 | CARB-2014v2 | CARB-2028 | Yes-UNC (T4.1)
WRAP Fossil EGU w/ CEM | WRAP-RB-EGU | WRAP-2028-EGU1 | Yes-Ramboll (T4.2)
WRAP Fossil EGU w/o CEM | WRAP-RB-EGU | WRAP-2028-EGU | Yes-Ramboll (T4.2)
WRAP Non-Fossil EGU | EPA-2016v1 | EPA-2028v1 | Yes-Ramboll (T4.2)
Non-WRAP EGU | EPA-2016v1 | EPA-2028v1 | No (EPA Platform)
O&G WRAP O&G States | WRAP-RB-O&G | WRAP-2028-O&G | Yes-UNC (T4.3)
O&G WRAP Other States | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.3)
O&G non-WRAP States | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.3)
WRAP Non-EGU Point2 | WRAP-2014v2 | EPA-2028v1 | Yes-Ramboll
Non-WRAP non-EGU Point | EPA-2016v1 | EPA-2028v1 | Yes-Ramboll
On-Road Mobile 12WUS2 | WRAP-2014v2 | WRAP-2028-Mobile | No (WRAP MS study)
On-Road Mobile 36US | EPA-2016v14 | EPA-2028v14 | No (EPA Platform)
Non-Road 12WUS2 | EPA-2016v1 | WRAP-2028-Mobile | No (WRAP MS study)
Non-Road non-WRAP 36US | EPA-2016v1 | EPA-2028v1 | No
Other (Non-Point) 12WUS2 | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.5)
Can/Mex/Offshore 12WUS2 | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.6)
Fires (WF, Rx, Ag) | WRAP-RB-Fires | WRAP-RB-Fires | No (already processed)
Natural (Bio, etc.) | WRAP-2014v2 | WRAP-2014v2 | No (2014v2)
Boundary Conditions (BCs) | WRAP-2014-GEOS5 | WRAP-2014-GEOS5 | Hold BCs Constant?
California ARB provided complete anthropogenic emissions for 2014v2 and 2028
CA 2014v2 used in Representative Baseline (RB)
Natural emissions held constant at 2014v2 levels for RB and 2028
WRAP-RB-Fires also constant between RB and 2028
Currently 2014v2 BCs based on WRAP 2014 GEOS-Chem held constant for RB and 2028 modeling
  Optional task to conduct GEOS-Chem with 2028 emissions and 2014 met

## Slide 21: RepBase & 2028 Electrical Generating Unit Emissions
Source Sector | Representative Baseline | 2028 OTB | 2028 SMOKE Required?
WRAP Fossil EGU w/ CEM | WRAP-RB-EGU | WRAP-2028-EGU1 | Yes-Ramboll (T4.2)
WRAP Fossil EGU w/o CEM | WRAP-RB-EGU | WRAP-2028-EGU | Yes-Ramboll (T4.2)
WRAP Non-Fossil EGU | EPA-2016v1 | EPA-2028v1 | Yes-Ramboll (T4.2)
Non-WRAP EGU | EPA-2016v1 | EPA-2028v1 | No (EPA Platform)
WRAP Fossil-Fuel EGUs with CEM (CAMD) and w/o CEM data from WRAP EGU Emissions Analysis Project (CNEE) [WRAP-EB_EGU & WRAP-2028-EGU]
WRAP Non-Fossil-Fuel EGUS from EPA-2016v1 (RB) and EPA-2028v1 (2028)
EGU from non-WRAP states from EPA-2016v1 (RB) and EPA-2028v1 (2028)

## Slide 22: RepBase and 2028 Oil and Gas and Non-EGU Point
Source Sector | Representative Baseline | 2028 OTB | 2028 SMOKE Required?
O&G WRAP O&G States | WRAP-RB-O&G | WRAP-2028-O&G | Yes-UNC (T4.3)
O&G WRAP Other States | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.3)
O&G non-WRAP States | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.3)
WRAP Non-EGU Point2 | EPA-2016v1 | EPA-2028v1 | Yes-Ramboll
Non-WRAP non-EGU Point | EPA-2016v1 | EPA-2028v1 | Yes-Ramboll
O&G in 7 of 8 O&G WRAP states (CO, MT, ND, NM, SD, UT, WY) from WRAP OGWG Study
  O&G for CA (8th WRAP state) from CARB
O&G in remainder non-O&G WRAP states from EPA 2016v1 platform
Non-EGU Point from EPA 2016v1 platform (EPA-2016v1 & EPA-2028v1)
  WRAP state updates as available
  Consideration of using WRAP-2014v2 for both RB and 2028

## Slide 23: Mobile, Other (Non-POINT) and Mex/Can
Source Sector | Representative Baseline | 2028 OTB | 2028 SMOKE Required?
On-Road Mobile 12WUS2 | WRAP-2014v2 | WRAP-2028-Mobile | No (WRAP MS study)
On-Road Mobile 36US | EPA-2016v14 | EPA-2028v14 | No (EPA Platform)
Non-Road 12WUS2 | EPA-2016v1 | WRAP-2028-Mobile | No (WRAP MS study)
Non-Road non-WRAP 36US | EPA-2016v1 | EPA-2028v1 | No
Other (Non-Point) 12WUS2 | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.5)
Can/Mex/Offshore 12WUS2 | EPA-2016v1 | EPA-2028v1 | Yes-UNC (T4.6)
WRAP Mobile Study for on-road and non-road in 12WUS2 domain
  Includes SMOKE-MOVES with 2028 MOVES EF and 2014 WRF Met
For EUSA 36US domain, EPA 2016v1 and 2028v1 for RB and 2028
  Means using 2016 met-adjusted on-road mobile in EUSA with 2014 modeling platform
EPA 2016v1 and 2028v1 for Other (non-Point) and Mex/Can

## Slide 24: Task 6: Verification of 2014v2 Platform on IWDW
Objective: Test to verify/set-up of 2014v2 and subsequent modeling scenarios’ file data transfers to IWDW to be available for distribution.
  Transfer of WRAP 2014v2 modeling files (and subsequent scenarios) to IWDW
  IWDW set up server with sufficient memory and cores (24+) to replicate PGM modeling
  Ramboll remotely accesses IWDW server and re-run PGM modeling form portions of modeling period
  Compare results with PGM results from Ramboll Linux Farm to make sure achieves acceptable level of differences
  Make available 2014v2 modeling platform files for distribution on the IWDW

## Slide 25: Next steps: WRAP 2014 Shake-out Phase IV SOW
Update WRAP 2014 Shake-Out Phase IV Scope-of-Work (SOW)
  Refine SOW for 3 New Tasks:
    Task 4: Dynamic Evaluation Modeling
    Task 5: 2028 OTB/OTW Emissions and CAMx Modeling
    Task 6: 2014v2, RepBase and 2028OTB Verification on IWDW Servers and IWDW Support
  Add costs and schedule for WRAP Phase IV work effort

## Slide 26: WRAP 2014 Shake-Out Phase III and IV Schedule