## Slide 1: Quarterly Update on the National Inventory Collaborative
September 20, 2018
DRAFT

## Slide 2: Webinar Ground Rules: Questions?
Each workgroup will give a 7 minute update introducing their group and their plans for the coming months.
All call participants will remain on mute during the webinar.
Type your questions into the question box on the webinar client.
We will try to answer questions at the end of the webinar.
We will create a Q&A document following the webinar and post with the meeting notes on the Collaborative Wiki: http://views.cira.colostate.edu/wiki/wiki/9169

## Slide 3: Overview of the Platform Collaborative
A new multi-purpose emissions modeling platform (EMP) based on the 2014 National Emissions Inventory version 2 (2014NEIv2) is needed
  State Implementation Plans, federal analyses
  For the first time, EPA, states, and MJOs are engaging in collaborative EMP development
  The 2016 base year was selected via a collaborative process
Future years selected due to regulatory relevance
  2023 is relevant for Ozone NAAQS moderate areas
    Although 2020 is relevant for 2015 O3 NAAQS marginal areas, modeling is not required for marginal areas; 2020 is relevant for 2008 O3 NAAQS reclassifications
  2028 for regional haze

## Slide 4: 2016 EMP Schedule
Several versions of 2016 platform will be developed
  Alpha: preliminary version based on 2014NEIv2 for some and 2016 for other key sectors (released May 2018)
    ftp://newftp.epa.gov/Air/emismod/2016/alpha/
    Compatible versions of 2014 and 2015 were also released
    For initial testing of 2016 model runs
  Beta: improved and/or new version of actual 2016 emissions for most sectors and preliminary projected emissions to 2023 and 2028 (October 2018)
  V1.0: fully updated 2016 emissions and complete projected emissions for 2023 and 2028 (Early 2019)
Schedule overlaps with 2017 NEI Development
  Prioritize the 2017 NEI over the 2016 platform, as needed
  Any missing data for 2016 will be filled in based on 2014 NEI data and nationally consistent methods

## Slide 5: Organizational Structure
Coordination co-leads: Zac Adelman (LADCO) and Alison Eyth (EPA OAQPS)
  Developed process and communication structures, facilitate discussions, help resolve issues, documentation requirements, coordinate distribution of data to stakeholders
Coordination committee: regional, state, EPA leaders
  Define processes, resolve issues, co-lead workgroups
  Includes overall and WG co-leads plus MJO directors
Sector-specific Workgroups: one regional/state staff and one EPA staff (where possible)
  Focus on preparing emissions estimates for 2016 and future years, plus improve how the emissions sectors are modeled
  Include participants from EPA/states/locals/regions

## Slide 6: Collaborative Workgroup Reports
EGUs
Non-EGU Point
Nonpoint
Oil and gas sources (point and nonpoint)
Onroad
Nonroad
Rail
Commercial Marine Vessels (CMV)
Fires
Biogenics
Modeling
Wrap up/Next steps
Wiki has more information and notes from each workgroup
  http://views.cira.colostate.edu/wiki/wiki/9169

## Slide 7: Electricity Generating Units (EGU) Workgroup
Co-leads: Julie McDill (MARAMA), Serpil Kayin (EPA CAMD), Alison Eyth (EPA OAQPS)
Schedule: Calls 4th Thursday at 2:00pm ET
Wiki: http://views.cira.colostate.edu/wiki/wiki/9174

## Slide 8: EGU Workgroup: 2016 beta
Approach:
  States submitted 2016 emissions for at least Type A sources
  EPA collated and quality assured emissions and released inventory in June
  Minor updates made post-June at request of a few states
  States and EPA worked together to finalize EIS unit matches to CEMS data (CAMD/ORIS IDs), NEEDS IDs (to separate EGUs from non-EGUs), and ERTAC
  Temporal profiles for EGUs without CEMS being developed
Status:
  2016 emissions will be final once the cross-reference is finalized
  2023 and 2028 emissions based on ERTAC-EGU and IPM being evaluated
Milestones:
  Finalize cross-reference and temporal profiles over next few weeks
  2016 emissions available by end of October
  Develop future year projections by October-November

## Slide 9: 2014 and 2016 EGU Summary
Chart: 2014 and 2016 EGU emissions
| NOx | SO2 | PM2.5
2014v2 EGU | 1759400.4077 | 3249656.3429 | 182912.7409
2016 Draft EGU | 1420558.1197 | 1623498.9362 | 149919.7997
2016 June EGU | 1318421.084 | 1567766.6421 | 133438.2935
Chart: 2016 EGUs with CEMS vs non-CEMS
| March nonCEMS | June nonCEMS | March CEMS | June CEMS
NOx | 104509.5095 | 106095.2374 | 1209953.3728 | 1212325.8466
SO2 | 44122.4585 | 52282.055 | 1527094.4228 | 1515484.5871
PM2.5 | 8910.6944 | 9097.0898 | 131912.0155 | 124341.2037
There was a substantial EGU NOx and SO2 drop from 2014-2016 The vast majority of annual EGU emissions are from units with CEMS
Many Non CEMS sources are peakers and may contribute substantially on HEDD

## Slide 10: EGU Workgroup: ERTAC-EGU
State review complete of
  ERTAC EGU V16.0 input files
  CONUS v16.0 output files
Runs with new inputs of CONUS v16.1underway
We will complete a CONUS v16.1 run for:
  Base year 2016 complete by end of October 2018
  Future year 2023 & 2028 complete by mid November 2018

## Slide 11: EGU Workgroup: IPM
EPA launched its updated Power Sector Modeling website in June 2018, equipped with
  Power Sector Modeling Resources
    IPM v6 with multiple case scenario runs and Results Viewer
    We are currently working on integrating latest input data and rules to the platform
  Power Sector Modeling Regulatory Applications
NEEDS now have quarterly updates (latest: 9/17/2018)
  https://www.epa.gov/airmarkets/clean-air-markets-power-sector-modeling

## Slide 12: Non-EGU Point Workgroup
Co-leads: Tammy Manning (NC DEQ), Caroline Farkas (EPA)
Schedule: Calls on 3rd Tuesday at 2:00pm Eastern
Wiki: http://views.cira.colostate.edu/wiki/wiki/9177

## Slide 13: Non-EGU Point Workgroup: 2016 beta
Status
  Working on reviewing Control and Projection packets
  Adding consent decrees to a new packet type (“allowable”)
  Reaching out for new sources of information, where needed
Milestones
  Expected review date: now through end of October
  Expected release date: November 1, 2018
  Expected projection inventory date: mostly November 1, 2018

## Slide 14: Non-EGU Point Workgroup: Projections
Aircraft – projecting 2014 EDMS estimates to 2016, 2023, and 2028 for beta; will update to new FAA model (AEDT) for v1
Corn Ethanol – keeping flat (no growth)
Consent decrees – working together to identify and add recent consent decrees using “allowable packet”
Cement manufacturing – working to find new source of projections
Closures – asking states to submit closures they know are occurring by 2028 or earlier.
Removing control packets that have compliance dates prior to 2014 (e.g., RICE NESHAP)

## Slide 15: NonPoint Workgroup
Co-leads: Caroline Farkas (EPA), Jennifer Snyder (EPA)
Schedule: Calls on 4th Monday at 2:00pm Eastern
Wiki: http://views.cira.colostate.edu/wiki/wiki/9178

## Slide 16: NonPoint Workgroup: 2016 beta
Status
  Open burning: awaiting contractor review of data – will be in v1, not beta
  Working on reviewing Control and Projection packets
  Reaching out for new sources of information where needed
Milestones
  Expected review date: now-end of October
  Expected release date: November 1, 2018
  Expected projection inventory date: mostly November 1, 2018

## Slide 17: NonPoint Workgroup: Projections
Population-based Sectors - Awaiting new population data from EPA tool (ICLUS)
Fugitive Dust - No growth for unpaved roads
Agricultural Sources - Working on finalizing livestock projections
Control packets – reviewing and updating as needed, removing if full compliance date is prior to 2014

## Slide 18: Oil & Gas Workgroup
Co-leads: Jeff Vukovich (EPA), Tom Moore (WESTAR and WRAP)
Schedule: Calls on 2nd Monday at 2:00pm Eastern
Wiki: http://views.cira.colostate.edu/wiki/wiki/9180

## Slide 19: Oil & Gas Workgroup: 2016 beta
Add content

## Slide 20: Onroad Mobile Workgroup
Co-leads: Julie McDill (MARAMA), Alison Eyth (EPA OAQPS)
Schedule: Calls 3rd Thursday at 2:00pm ET
Wiki: http://views.cira.colostate.edu/wiki/wiki/9181
Summary reports and maps for beta:
  ftp://newftp.epa.gov/Air/emismod/2016/beta/reports/onroad/

## Slide 21: Onroad Mobile Workgroup
Approach:
  Beta emission factors output from MOVES2014a and compatible with 2014NEIv2 inputs but run for 2016, 2023, and 2028
  For beta, states provided base and future year activity data; for non-submitting states, activity data projected from 2014NEIv2 to 2016, 2023, 2028
  Spatial surrogate updates: On-network spatial surrogates updated using 2016 data, long-haul combination truck surrogate updated using state inputs
Status:
  2016 emissions are available
  Activity data projections method for 2023 and 2028 being developed
  2023 and 2028 emissions coming soon
Milestones:
  Release 2016 data this week
  Develop and quality assure 2023 and 2028 data by end of October
  V1.0 will use emission factors based on updated age distributions and populations and be available late 2018/early 2019

## Slide 22: 2016 beta Onroad Emissions Totals
Chart: Onroad CAP Emissions in 2014 and 2016
| NH3 | NOX | PM10 | PM2_5 | SO2 | VOC
2014v2 | 107683.9754 | 4835396.3777 | 301466.744 | 161732.3515 | 28093.877 | 2346619.7922
2016fd alpha | 101229.6826 | 4045836.1123 | 272854.8825 | 130262.6496 | 27355.6972 | 1961994.539
2016ff beta | 100840.8006 | 4057271.549 | 272878.9779 | 130662.7728 | 27262.1529 | 1950603.2851
Pollutant | 2014v2 | 2016fd alpha | 2016ff beta | 2016 beta- 2014v2 % change | 2016 alpha-beta % change
NH3 | 107,684 | 101,230 | 100,841 | -6% | -0.4%
NOX | 4,835,396 | 4,045,836 | 4,057,272 | -16% | 0.3%
PM10 | 301,467 | 272,855 | 272,879 | -9% | 0.0%
PM2_5 | 161,732 | 130,263 | 130,663 | -19% | 0.3%
SO2 | 28,094 | 27,356 | 27,262 | -3% | -0.3%
VOC | 2,346,620 | 1,961,995 | 1,950,603 | -17% | -0.6%
CO | 24,141,986 | 20,446,327 | 20,345,829 | -16% | -0.5%
Credit: US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 23: Total 2016 beta Onroad NOx
Credit: US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 24: Surrogate Update: On-network
Credit: US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 25: 2016 beta Hoteling Surrogate and Emissions

## Slide 26: Nonroad Mobile Workgroup
Co-leads: Rebecca Simpson (Colorado Department of Public Health and Environment), Sarah Roberts (EPA OTAQ)
Schedule: Calls on 4th Thursday at 3:30pm Eastern
Wiki: http://views.cira.colostate.edu/wiki/wiki/9179
Status of the 2016 Beta Inventory: newly-released MOVES2014b will be used to generate the beta nonroad inventory and projections.

## Slide 27: Nonroad Mobile Workgroup
Approach: EPA running MOVES2014b for the 2016 beta inventory and projections. Work group consensus to not include state-supplied data in the beta inventory, so that states can have the opportunity to review updated nonroad model defaults.
Status: MOVES2014b was released August 28th; model runs initiated this week. Work group concurrently working on updating the surrogate data used to allocate national- and state-level equipment populations to counties.
Milestones: aiming to release 2016 nonroad beta inventory and projections in October. Updated geographic surrogates for v1 complete by January 2019.

## Slide 28: Nonroad Mobile Workgroup Updating Geographic Allocation of Equipment (v1)
Workgroup wants to improve the equipment populations of the highest-emitting nonroad categories: Construction, Agriculture, Lawn & Garden, and Recreational.
Nonroad equipment population data, however, are scarce. More feasible to adjust the model’s equipment population growth rates and/or how the model allocates national equipment populations to the county level.
MOVES2014b includes updated equipment population growth rates, so the work group is focusing on updating geographic allocation factors. Volunteers from NC, GA, CO, MA, Pima County, and EPA are researching and evaluating data sources (e.g., USDA Census of Agriculture and Farm Production Expenditures, EIA Fuel Oil and Kerosene Sales, U.S. Census Bureau County Business Patterns, NASA, CARB surveys).

## Slide 29: Rail Workgroup
Lead Mark Janssen (LADCO)
Schedule: Calls 3rd Thursday at 11:00am ET
Wiki: http://views.cira.colostate.edu/wiki/wiki/9182
Status of the 2016 beta Inventory
  Expected completion is October 31
  2017 NEI estimates by November
  Will include a SMOKE Linkproc format for link-based processing

## Slide 30: Rail Workgroup: 2016 beta
Emissions calculated for Class 1 & 2/3 line haul
  Link-level estimates for Class 1 Line Haul (85% rail NOx emissions).
  Similar to traditional methods
Integrating sources for rail yard estimates
  Complete upgrade from past inventories: UP, BNSF, KCS
  LADCO/IL/MI gap filled CP and CN
  GA and ME filling in NS and CSX
  Need state help filling in gaps by looking at Google Earth: counting switching engines
Class 2/3 and commuter rail estimates were updated for some states. Can be significant
  Company specific Fleet Mix and link level also possible.
  Including AMTRAK in Class 2/3

## Slide 31: Commercial Marine Vessel (CMV) Workgroup
Lead Mark Janssen (LADCO)
Schedule: Calls 3rd Tuesday at 3:00PM ET
Wiki: http://views.cira.colostate.edu/wiki/wiki/9176
2016 beta = 2016 alpha = 2014v2
Status of the 2016 Version 1 Inventory
  Expected completion is February 2019
  EPA will build 2017 NEI estimates for Ocean going (Category 3) vessels for December deadline
  Will include a SMOKE Linkproc format for link-based processing

## Slide 32: CMV Workgroup: Methodology
OTAQ finished draft power model to calculate Class 3 large vessel power
  Model released to beta testers
  Read AIS data and do spatial attribute checking
OAQPS has a work assignment to build the 2017 NEI inventory for marine from AIS. This will include Category 1 and 2 (Ocean/Great Lakes/Rivers) and Tugs at ports.
Workgroup will use these tools/methods to generate 2016 estimates in parallel with 2017

## Slide 33: Fire Workgroup
Co-leads: Jeff Vukovich (EPA), Tom Moore (WESTAR)
Schedule: Calls on 1st Thursday 1PM ET
Wiki: http://views.cira.colostate.edu/wiki/wiki/9175
Google Drive: https://drive.google.com/drive/folders/14e4iqUv64z1eC71BHyYPaj09I-kt1MBW
Includes wildfires, prescribed fires and agricultural burns

## Slide 34: Fire Workgroup: 2016 beta
New data acquired
  Seven states and one tribe voluntarily submitted fire activity and/or emissions data (CO, GA, ID, KS, MN, NC, WA and Nez Perce tribe)
  National fire information and polygon data acquired
    National Association of State Foresters (NASF): wildfires
    ICS-Planned Ignition Release (PIR) data: prescribed fires
    Monitoring Trends in Burn Severity (MTBS) shapefiles: wildfires and prescribed fires
Approach
  Continue to use SmartFire2 and BlueSky modeling framework (same versions as in 2016 alpha)
  Agricultural burns emissions estimates done separately (G. Pouliot)
  Implement new data in best way possible
  Update fuel-bed information in BlueSky (higher resolution and more current database (year 2014) data will be used)
  Grassland fires moved from Ag burn (Pouliot) processing to SmartFire2 + BlueSky modeling framework

## Slide 35: Fire Workgroup: 2016 beta
Status
  Processing has already begun using new data
  QA has also begun at various steps in the fire emissions modeling process
Milestones
  Expected review date: early October
  Expected release date: October 31, 2018
Projections:
  None planned; possible for 2016v1

## Slide 36: Biogenics Workgroup
Co-leads: Jeff Vukovich (EPA), Doug Boyer (TCEQ)
Schedule: Calls on 3rd Tuesday 330PM ET
Wiki: http://views.cira.colostate.edu/wiki/wiki/9172
Google Drive:
  https://drive.google.com/drive/folders/1ulLmJPQ1WkOnsi6_g2nkHLWfqJEw4RSU

## Slide 37: Biogenics Workgroup: 2016beta
Models
  Biogenic Emissions Inventory System version 3.61 (BEIS3)
  Model of Emissions of Gases and Aerosols from Nature (MEGAN) version 3 beta
Approach
  Execute annual simulations for both BEIS3 and MEGANv3
  Examine and quality assess input data (e.g. landuse)
  Emissions comparisons
  Research availability of emissions flux observational data

## Slide 38: Biogenic Workgroup: 2016 beta
Status
  MEGANv3 beta “default” configuration run complete
  BEIS3 run complete
    Considering small landuse change and rerun in short-term
  Quality assurance steps and comparisons continue
Milestones
  Expected release date: October 31, 2018
  Release will include both BEIS3 and MEGANv3 gridded emissions
Projections:
  None planned

## Slide 39: Emissions Modeling Workgroup
Co-leads: Husain Waheed (MD Dept of Environment), Zac Adelman (LADCO) [Interim]
Schedule: No call schedule yet, starting in October 2018
Wiki: http://views.cira.colostate.edu/wiki/wiki/9190
Objectives:
  Gather, test, and prepare the emissions data platforms created by each of the inventory sector workgroups for use in air quality modeling.
  Produce an emissions modeling platform for modeling 2016 and projection years.

## Slide 40: Modeling Workgroup: Tasks
Testing and Platform Development
  Assess availability of 2016 meteorology
  Emissions modeling protocol and platform creation
  SMOKE modeling
  Data validation
Platform Packaging
  Create an emissions modeling package with data and software needed to prepare the emissions for air quality modeling
  Develop an approach (and document) how to customize the base emissions modeling platform
Documentation and Evaluation
  Provide feedback to inventory sector workgroups on their documentation
  Model performance evaluation of the 2016 base modeling
  Create best-practices guidance for using the Collaborative data for modeling

## Slide 41: Inventory Collaborative Next Steps
Workgroups will be prioritizing their work to produce version 1.0 of the 2016 inventory by spring 2019; including projections to 2023 and 2028
Collecting information on prospective uses of the alpha and beta platforms: let us know
Quarterly outreach calls by the Collaborative to report out on progress: mark your calendar
Next outreach call:
December 19 at 12:00 Eastern

## Slide 42: Inventory Collaborative Wiki
These slides, answers to the questions posed during this webinar, notes:
http://views.cira.colostate.edu/wiki/wiki/9193
Main National Inventory Collaborative Wiki includes live workgroup wikis, documentation, calendar:
http://views.cira.colostate.edu/wiki/wiki/9169