## Slide 1: Modeling Performance Evaluation and Sensitivity Overview
Heather Simon, Norm Possiel, Shannon Koplitz, Sharon Phillips, Barron Henderson, Brett Gantt
U.S. EPA OAQPS

## Slide 2: EPA OAQPS Modeling Set-up for 2016v1
Annual model simulations with CMAQv5.3.1 and CAMxv7 beta6
  CB6r3 chemical mechanism
  POA treated as non-volatile (did not use VBS)
  No bidirectional ammonia flux
Nested 36km and 12km domains with 35 vertical layers
  Potential 4 km modeling for domains (NE/MW/CA)
Meteorology from WRFv3.8
Initial and Boundary Conditions from
  Hemispheric CMAQv5.2.1 with 2016fe emis
See extra slides for additional details
36km
12km

## Slide 3: Completed model sensitivity runs
CMAQ
  Multiple deposition schemes & with and without Bidirectional NH3 flux
  Various meteorological options and PBL schemes in WRF
  GEOS-Chem boundary conditions
  Updated VOC speciation
  Lightning NO
CAMx
  Vertical diffusivity, “Kv”, sensitivities
  Ammonia deposition sensitivities
  GEOS-Chem boundary conditions

## Slide 4: Model Performance Framework
Performance broken out into different spatial and temporal scales
  Spatial: NOAA climate region
  Temporal:
    Winter (DJF), Spring (MAM), Summer (JJA), Fall (SON)
    Ozone season (May-September)
Pollutants
  PM2.5 components (sulfate, nitrate, OC, EC)
  Ozone, with focus on days > 60 ppb
  NOx (see extra slides)
Highlights given from base CMAQ and CAMx Simulations and from key sensitivity simulations
Results are still preliminary – this is a work in progress

## Slide 5: PM2.5

## Slide 6: Measured PM composition across the US (2013-2015)
Winter
Summer
Composition varies by location but there are some overarching seasonal patterns
Winter: Major components of PM2.5 are nitrate, sulfate and OC
Summer: Major components of PM2.5 are sulfate and OC (nitrate still important in CA)

## Slide 7: Sulfate spatial patterns in CMAQ and CAMx
Base CAMx
Base CMAQ
January
July
Focus evaluation on locations with high sulfate concs
Winter: entire Eastern US
Summer: Ohio River Valley

## Slide 8: Sulfate Bias (%) – Overview
CMAQ 2016fh
CAMx 2016fh
Sulfate overprediction in the Western US where concentrations are very low – very small absolute bias
Winter Eastern US: CAMx bias is mostly between -20% and +40%, CMAQ underpredictions are generally less than -20%
Summer Ohio River Valley: CAMx bias is between -20% and +20%, CMAQ bias is between -40% and -20%

## Slide 9: Sulfate – 2016fh National NMB (%)
CAMx
CMAQ
Winter
Summer
Sulfate overprediction in the Western US where concentrations are very low – very small absolute bias
Winter Eastern US: CAMx bias is mostly between -20% and +40%, CMAQ underpredictions are generally less than -20%
Summer Ohio River Valley: CAMx bias is between -20% and +20%, CMAQ bias is between -40% and -20%

## Slide 10
NoahYSU - Base
January
July
Key Sulfate Sensitivity Simulations
STAGE - Base
GEOSChem - Base
Base run sulfate overprediction in the Western US where concentrations are very low – very small absolute bias
Winter Eastern US: Base run CAMx bias is mostly between -20% and +40%, Base run CMAQ underpredictions are generally less than -20%
Summer Ohio River Valley: Base run CAMx bias is between -20% and +20%, Base run CMAQ bias is between -40% and -20%

## Slide 11: Nitrate spatial patterns in CMAQ and CAMx
Base CAMx
Base CMAQ
Focus evaluation on locations with high nitrate concs
Winter: Midwest US and California
  Note both models miss high winter nitrate in Salt Lake City
Spring: Midwest US
Summer (not shown): California
January
April

## Slide 12: Nitrate Bias (%) – Overview
California (West region) underpredicted year-round in both models
Winter Eastern US : Midwest shows underpredictions up to 20%, Northeast corridor shows overpredictions in both models , underpredictions in SW (including SLC), performance in both models look similar
Spring Midwest: CMAQ is underpredicted, CAMx bias is between -20% and + 20%
CMAQ 2016fh
CAMx 2016fh

## Slide 13: Nitrate – 2016fh National NMB (%)
CMAQ
Winter
Spring
CAMx
California (West region) underpredicted year-round in both models
Winter Eastern US : Midwest shows underpredictions up to 20%, Northeast corridor shows overpredictions in both models , underpredictions in SW (including SLC), performance in both models look similar
Spring Midwest: CMAQ is underpredicted, CAMx bias is between -20% and + 20%

## Slide 14
14
Key Nitrate Sensitivity Simulations: CAMx
January
GEOSChem - Base
Rscale - Base
BiDi - Base
April
California (West region) underpredicted year-round in both base run model simulations
Winter Eastern US base model runs: Midwest shows underpredictions up to 20%, Northeast corridor shows overpredictions in both models, underpredictions in SW (including SLC), performance in both models look similar
Spring Midwest: Base run CMAQ is underpredicted, Base run CAMx bias is between -20% and + 20%

## Slide 15
15
15
Key Nitrate Sensitivity Simulations: CMAQ
January
BiDi (M3DRY)- Base
BiDi (STAGE)- Base
NoahYSU- Base
April
California (West region) underpredicted year-round in both base run model simulations
Winter Eastern US base model runs: Midwest shows underpredictions up to 20%, Northeast corridor shows overpredictions in both models, underpredictions in SW (including SLC), performance in both models look similar
Spring Midwest: Base run CMAQ is underpredicted, Base run CAMx bias is between -20% and + 20%

## Slide 16: OC spatial patterns in CMAQ and CAMx
Base CAMx
Base CMAQ
January
July
Focus evaluation on locations with high OC concs
Winter: Eastern US and California
  Note both models miss high winter nitrate in Salt Lake City
  Winter OC mostly from primary emissions and woodsmoke
Summer: Southeastern US and California
  Summer OC mostly from SOA and fires

## Slide 17: Organic Carbon Bias (%) – Overview
Both models show large overestimates for most regions (except the West) and seasons
Winter underestimates in California (hard to model stable mixing conditions in San Joaquin Valley using 12km resolution modeling)
CMAQ 2016fh
CAMx 2016fh

## Slide 18
Organic Carbon Recent Science Updates
OAQPS has traditionally run CMAQ using non-volatile POA and no pcSOA
CMAQ developers in EPA Office of Research and Development have been working on numerous science updates for modeling organic carbon
They report less overpredictions in OC using their most up-to-date treatment
CMAQ 2016fh - OAQPS
CMAQ 2016fh - ORD

## Slide 19: EC Bias (%) – Overview
EC performance has improved since 2015, likely related in part to fire speciation updates
CMAQ 2016fh
CAMx 2016fh

## Slide 20: PM2.5 performance key takeaways
Sulfate
  CAMx:
    bias is mostly between -20% and +40% in winter/Eastern US
    bias is between -20% and +20% in summer/Ohio River Valley
  CMAQ:
    underpredictions are generally less than -20% in winter/Eastern US
    bias is between -40% and -20% in summer/Ohio River Valley
Nitrate:
  CMAQ
    Winter Midwest shows underpredictions up to 20%, Northeast corridor shows overpredictions, underpredictions in SW
    Spring underpredictions across entire US
    Using STAGE and M3DRY bi-direction ammonia flux improve performance
  CAMx
    Winter Midwest shows underpredictions up to 20%, Northeast corridor shows overpredictions, underpredictions in SW
    Spring CAMx bias is between -20% and + 20%
  Both models: Underestimates in California at 12km resolution
OC overestimates across all regions/seasons in both models
    More investigation needed
  Underestimates in California at 12km resolution
EC performance generally shows bias withing +/-20% in most regions/season
CSN
CMAQ
CAMx
Annual CONUS CSN PM2.5

## Slide 21: Ozone

## Slide 22
CAMx
CMAQ
<= AQS =>
Sites
<= CASTNet =>
Sites
Region/Season Mean Bias
MDA8 > 60 ppb
Notes: Spring - AQS
CAMx: MB is generally underpredicted in the range of 10 to 20 ppb in the Upper Midwest and in the western US regions.
CMAQ: MB is generally underpredicted in the range of 10 to 20 ppb in all regions
Summer – AQS
MB for CAMx and CMAQ is within + 10 ppb in most regions.
Spring/Summer – CASTNet
CMAQ shows under prediction in the range of 10 to 20 ppb in more regions that CAMx.

## Slide 23
MDA8 O3 Monthly Box Plots by Region
CMAQ =>
CAMx =>
Northeast
Ohio Valley
Midwest
20 ppb
100 ppb
20 ppb
100 ppb
Notes: Both CAMx and CMAQ under predicted MDA8 O3 during the winter and spring in all three regions. The under prediction is greater with CAMx than CMAQ.
In the Midwest and Ohio Valley, the inter-quartile range of observed values declines notably between April/May/June and July/August/September.
The CAMx and CMAQ predictions also decline beginning in July, but not to the extent of the observed data.
In the Northeast, the observed values peak in July as do the model predictions

## Slide 24
May – September MDA8 O3 > 60 ppb
<= Mean =>
Bias
<= Normalized =>
Mean
Bias
CMAQ
CAMx
Notes: Most notable difference in performance between the two models is that CAMx shows less under prediction bias in the area from Texas northeastward across the south and Ohio Valley, up to and along the NE Corridor.
Elsewhere both models tend to show similar performance.

## Slide 25
CAMx May – September MDA8 O3 > 60 ppb
2011 & 2016
<= Mean =>
Bias
<= Normalized =>
Mean
Bias
2011
2016
Notes: The performance in the western portion of the US seems in 2016 seems to be fairly consistent with the performance in 2011, overall.
In the East, the tendency for over prediction from the Southeast to the Northeast in 2011 is not evident in 2016. However, in 2016 model bias is somewhat greater compared to 2011 in portions of the Midwest.

## Slide 26
MDA8 O3 Density Scatter Plots by Region for Summer
Midwest
Ohio Valley
Northeast
Midwest
Ohio Valley
Northeast
CMAQ =>
CAMx =>
Notes: In these three regions, CMAQ has a higher density of pairs along the 1:1 line, compared to CAMx.
However, obs/predicted pairs for CAMx tend to follow more closely the 1:1 line throughout the distribution more so that CMAQ.
Also, while CMAQ tends to under predict the upper end of the distribution, CAMx tends to over predict in this range.

## Slide 27
West
Southwest
Southeast
West
South
Southeast
CMAQ =>
CAMx =>
South
Southwest
MDA8 O3 Density Scatter Plots by Region for Summer
Notes: The differences between CMAQ and CAMx for the Southeast and South regions are similar to what we see in the Northeast and Ohio Valley regions.
In the Southwest, the obs values at the low end of the distribution are higher by 20 ppb or so compared to the obs values in other regions. Both models capture this regional characteristic.
In the West, both models under predict at the high end of the distribution – driven largely by the obs/predicted pairs in California.

## Slide 28
Select ozone Sensitivities: Ohio Valley Region
Notes: GEOS-Chem and Noah-YSU sensitivities increases ozone making underpredictions in May/June better and overpredictions in Jul-Sep worse
Speciation, kzmin and WRFv411 sensitivities have little impact

## Slide 29
Select ozone sensitivities: Northeast Region
Notes: GEOS-Chem sensitivity increases ozone making underpredictions in May/June better and overpredictions in Jul-Sep worse
Speciation, kzmin, Noah-YSU and WRFv411 sensitivities have little impact

## Slide 30
Select ozone sensitivities: South Region
Notes: GEOS-Chem and Noah-YSU sensitivities increases ozone making overpredictions in Jul-Sep worse
Speciation, kzmin and WRFv411 sensitivities have little impact

## Slide 31
Select ozone sensitivities: Southwest Region
Notes: GEOS-Chem and Noah-YSU sensitivities increases ozone making underpredictions better
Speciation, kzmin and WRFv411 sensitivities have little impact

## Slide 32: Findings
CMAQ and CAMx tend to under predict MDA8 ozone > 60 ppb during the spring and summer.
Both CAMx and CMAQ under predict MDA8 ozone > 60 ppb at individual monitoring sites nationwide; more so in the West compared to the East.
  CMAQ tends to have a greater regional extend of under prediction in the East compared to CAMx
Both models tend to under predict at the higher obs concentrations and over predict lower obs; CMAQ more so that CAMx
Both models under predict the seasonal increase in ozone from winter through spring, but over predict the drop in obs values in July-August-September in the Northeast, Ohio Valley, and Midwest.
Both models capture the April through October monthly temporal pattern in the Southeast and Southwest, with some under/over prediction depending on the month and model.
In the Southwest and West, both models tend to under predict the inter-quartile range of MDA8 in nearly all months
Sensitivity simulations
  GEOS-Chem and Noah-YSU sensitivities generally increase ozone making underpredictions better and overpredictions worse
  Other sensitivities had lesser impact on ozone bias

## Slide 33: Next steps
More in depth evaluation of CMAQ an CAMx sensitivity simulations
Evaluation of gas-phase precursors
  NOx (see extra slides)
  SO2
  CO
  VOCs

## Slide 34: Additional Slides

## Slide 35: EPA AQ Modeling Inputs and Set-up
component | Details | Reference
Emissions case | 2016v1 (2016fh)* | http://views.cira.colostate.edu/wiki/wiki/9169
Meteorology | WRF v3.8 | http://views.cira.colostate.edu/wiki/Attachments/Inventory%20Collaborative/Documentation/2016beta_0311/MET_TSD_2016.pdf
Meteorology post-processing | wrfcamx; MCIP v4.3 (“16j”) | http://www.camx.com/files/camxusersguide_v6-50.pdf; https://www.geosci-model-dev.net/3/243/2010/gmd-3-243-2010-discussion.html
IC/BC | 2016fe hemispheric CMAQv5.2.1 paired with CMAQ/CAMx 36US3 CONUS | https://cmascenter.org/conference//2018/slides/0850_henderson_hemispheric-cmaq_application_2018.pptx
Model (chemical mechanism) | CAMx v7 beta (cb6r4_CF); CMAQv5.3.1 (cb6r3/AERO7)** | http://www.camx.com/; https://www.epa.gov/cmaq/cmaq-models-0
domains | 36US3 & 12US2 CONUS | 
Layers | 35 vertical layers (no layer collapsing) | 
*With updates to CMV
**Note CMAQv5.3.1 bug preventing use of certain types of emissions files

## Slide 36: Base Simulation CMAQv5.3.1 Science Options
MECH [default: none] | cb6r3_ae7_aq
CTM_OCEAN_CHEM [default: Y] | Y
CTM_LTNG_NO [default: Y] | N
CTM_WB_DUST [default: N] | N
CTM_WVEL [default: Y] | N
KZMIN [default: Y] | Y
PX_VERSION [default: Y] | Y
NOAH_VERSION [default: N] | N
DepMod | M3DRY
CTM_MOSAIC [default: N] | N
CTM_BIDI_FERT_NH3 [default: Y] | N
CTM_ABFLUX [default: Y] | N
CTM_HGBIDI [default: N] | N
CTM_SFC_HONO [default: Y] | Y
CTM_GRAV_SETL [default Y] | Y
CTM_BIOGEMIS [default: Y] | N
Updated to AERO7for PM treatment; Marine halogen O3 destruction
Tested different configurations impact on mixing
Tested different bidi configurations

## Slide 37: CAMxv7.0 “beta 6” Science Options
Diagnostic_Error_Check | FALSE
Flexi_Nest | FALSE
Advection_Solver | PPM
Chemistry_Solver | EBI
PiG_Submodel | NONE
Probing_Tool | NONE
Chemistry | TRUE
Drydep_Model | ZHANG03
Bidi_NH3_Drydep | FALSE
Wet_Deposition | TRUE
ACM2_Diffusion | FALSE
Surface_Model | FALSE
Inline_Ix_Emissions | TRUE
Super_Stepping | TRUE
Gridded_Emissions | TRUE
Point_Emissions | TRUE

## Slide 38: WRF Set-Up
Model Version | v3.8
Physics Options | Pleim-Xiu land surface model; ACM v2 boundary layer scheme; Kain-Fritch; cumulus parameterization with moisture-advection trigger; Morrison double moment microphysics; RRTMG longwave and shortwave radiation schemes;
36 NOAM domain Initialization | 0.25-degree GFS analysis and 3-hour forecase from 00Z, 06Z, 12Z, 18Z
12 US domain Initialization | 12 km NAM; 40 km EDAS where NAM data were not available
Analysis Nudging | temperature, wind, and moisture above the boundary layer
Deep soil moisture initialization | ipxwrf program
Landuse and land cover | 36 NOAM domain: USGS; 12 US domain: 2011 NLCD
Sea surface temperatures | GHRSST at 1 km resolution
Other | Lightning data assimilation for characterizing deep convection

## Slide 39: NOx

## Slide 40: NOx spatial patterns in CMAQ and CAMx
CAMx
CMAQ
January
July

## Slide 41
CMAQ
CAMx
Unbiased or slightly underpredicted NOx in all regions for Fall/Winter/Spring in both CMAQ and CAMx
Summer bias between +/-20% except
  Slight overprediction in South for both models
  Slight overpredictions in Southeast for CAMx
  Slight underprediction in NRockiesPlains in both models
Overpredicted all seasons in the Northwest (only 2 monitors)

## Slide 42: Winter NOx NMB (%)
CMAQ
CAMx
Small to moderate underpredicted NOx in all regions for both CMAQ and CAMx
Overpredicted all seasons in the Northwest (only 2 monitors; Seattle monitor hard to model due to complex coastal meteorology)

## Slide 43: Summer NOx NMB (%)
CMAQ
CAMx
Slight overprediction in South for both models
Slight underprediction in NRockiesPlains in both models
Overpredicted all seasons in the Northwest (only 2 monitors; Seattle monitor hard to model due to complex coastal meteorology)

## Slide 44: Geos-Chem BCs Sensitivity Simulations: NOx
CAMx: GEOSChem - Base
CMAQ: GEOSChem - Base
January
July

## Slide 45: Additional CMAQ sensitivities: NOx
WRFv4.11 - Base
NoahYSU - Base
Lightning NO - Base
July
January

## Slide 46: PM2.5

## Slide 47: CSN speciated PM2.5 performance: Northeast
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 48: CSN speciated PM2.5 performance: Upper Midwest
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 49: CSN speciated PM2.5 performance: Ohio River Valley
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 50: CSN speciated PM2.5 performance: Southeast
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 51: CSN speciated PM2.5 performance: South
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 52: CSN speciated PM2.5 performance: Northern Rockies and Plains
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 53: CSN speciated PM2.5 performance: Northwest
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 54: CSN speciated PM2.5 performance: Southwest
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 55: CSN speciated PM2.5 performance: West
CSN
CMAQ
CAMx
Summer
CSN
CMAQ
CAMx
Winter

## Slide 56: CMAQ comparison to MODIS AOD: methods
RSIG
  Product: modis.mod43k.Optical_Depth_Land_And_Ocean
    AOD at 500nm
  Regrid: 12US2 via WCS
CMAQ
  Variable AOD_W550_ANGST from PHOTDIAG1
    Angstrom exponent interpolation between 381 and 607 nm
  Filter grid cells:
    Select approximate overpass times
    Select only successful retrieval time/grid cells.
Average all data to monthly resolution

## Slide 57: How does CMAQ compare to MODIS AOD?
AOD comparison methods in extra slides
Remer et al. 2005 suggest uncertainty at the
+- 0.05
+-15% AOD
So good performance
  CMAQ > (MODIS * 0.85 – 0.05)
  CMAQ < (MODIS * 1.15 + 0.05)
When |DIFF| < 0.05, good.
When |1 – RATIO| < 0.15, good
Comparisons with satellite products is still a work in progress
Notes: Remer et al. 2005 suggest uncertainty at the 15% +- 0.05tau