## Slide 1: WRAP 2014 Regional Modeling
WRF MPE Summary
Jeremiah Johnson
jjohnson@ramboll.com
Jan 31, 2019

## Slide 2: EPA vs WAQS WRF Configuration
WRF Option | 2014/2015 EPA | 2014 WAQS
Domains run | 12-km | 36/12/4-km
Microphysics | Morrison 2 | Thompson
LW Radiation | RRTMG | RRTMG
SW Radiation | RRTMG | RRTMG
Sfc Layer Physics | MM5 similarity | MM5 similarity
LSM | Pleim-Xiu | Noah
PBL scheme | ACM2 | YSU
Cumulus | Kain-Fritsch | 36/12-km Multi-scale Kain Fritsch
BC, IC Analysis Nudging Source | 12-km NAM | 12-km NAM
Analysis Nudging Grids | 12-km | 36/12-km
Obs Nudging | None | 4-km
Sea Sfc Temp | FNMOC | FNMOC

## Slide 3: EPA vs WAQS WRF Domains
EPA 12US1
WAQS 36/12/4 km

## Slide 4: EPA vs WAQS WRF MPE Approach
Evaluate EPA 12US1 and WAQS 12WUS2
  For 12US1, include observation sites within WAQS 12 km only
Quantitative Evaluation
  METSTAT – model/obs pairing, bias/error statistics against NCAR ds3505 observations
    Soccer plots – monthly stats
    Time series – hourly and daily
    Plots for whole domain (12WUS2), all sites in a given state, and each individual site within each state
Qualitative Evaluation
  PRISM precipitation spatial maps
    Monthly and daily

## Slide 5: WRF Statistical Benchmarks
Meteorological Variable | Simple Conditions |  | Complex Conditions | 
 | Bias | Error | Bias | Error
Temperature | < ±0.5 °C | < 2.0 °C | < ±2.0 °C | < 2.5 °C
Wind Speed | < ±0.5 m/s | < 2.0 m/s (RMSE) | < ±1.5 m/s | < 2.5 m/s (RMSE)
Wind Direction | < ±10 degrees | < 30 degrees | < ±10 degrees | < 50 degrees
Humidity | < ±0.8 g/kg | < 2.0 g/kg | < ±1.0 g/kg | < 2.0 g/kg

## Slide 6: Soccer Plots – Wind Speed
EPA 12 km
WAQS 12 km
Most months within simple conditions goal for both runs
EPA run has slight overprediction bias for most months; WAQS slight underprediction

## Slide 7: Soccer Plots – Wind Direction
EPA 12 km
WAQS 12 km
WAQS outperforms EPA with overall lower bias; error is similar

## Slide 8: Soccer Plots – Temperature
EPA 12 km
WAQS 12 km
EPA run outperforms WAQS
WAQS temperature poorest for Jan-Apr with cold bias

## Slide 9: Soccer Plots – Humidity
EPA 12 km
WAQS 12 km
WAQS run outperforms EPA; both runs have positive (wet) bias for all months
EPA performance poorest for May-Oct: overactive convection?

## Slide 10: Soccer Plots – Humidity for all AZ sites
EPA 12 km
WAQS 12 km
WAQS run outperforms EPA; both runs have wet bias in Jul-Aug monsoon period

## Slide 11: Time Series – 2014 Q3 Humidity at KPHX
Aug 2

## Slide 12: Daily Precipitation Plots – Aug 3, 2014 (end 5 AM MST)
PRISM Obs
EPA 12 km
WAQS 12 km

## Slide 13: Monthly Precipitation Plots – Aug 2014
PRISM Obs
EPA 12 km
WAQS 12 km

## Slide 14: Monthly Precipitation Plots – Jan 2014
PRISM Obs
EPA 12 km
WAQS 12 km

## Slide 15: Daily Precipitation Plots – Jan 31, 2014
PRISM Obs
EPA 12 km
WAQS 12 km
Excellent agreement in spatial extent for both runs
Slight overestimation in magnitude for both runs, WAQS a bit better

## Slide 16: Summary and Conclusions
WRF performance reasonable for both simulations
  No obvious/egregious errors that would prevent use of either WRF simulation for AQ modeling
Not possible to know which WRF simulation will perform better in CAMx/CMAQ
  Relative performance varies across parameters/seasons/locations
  Best (or worst) performing WRF days may have small (or large) influence on AQ concentrations
  Other meteorological variables (vertical diffusion, PBL heights, etc.) may be more important than the ones we can easily evaluate (T, Q, winds, precip)
However, general performance tendencies
  EPA – wet bias in summer months associated with overactive summer convection; WAQS smaller wet bias
  WAQS – cold bias in Jan-Apr
  EPA and WAQS – good precipitation performance outside of summer months
All products (soccer plots, time series, precip maps) available for transfer to IWDW