## Slide 1
Southern New Mexico Ozone Modeling Study
Task 12: Ozone Source Apportionment Modeling
Ramboll-Environ (RE)
University of North Carolina (UNC-IE)
September 8, 2016

## Slide 2: SNMOS Background and Objectives
The southern Doña Ana County region has the highest ozone levels of any area in New Mexico
  The southern Doña Ana County area is within 95% of the federal standard for ozone
  The New Mexico Air Quality Control Act requires the New Mexico Environment Department to develop a plan for reducing ozone levels in areas that are within 95% of the ozone standard
The first step towards developing the plan is to understand the causes of high ozone in Doña Ana County
SNMOS objectives:
  Study the factors contributing to high ozone in Doña Ana County
  Investigate future emissions scenarios that will produce attainment of the ozone standard

## Slide 3: Overview of Approach
SNMOS builds off of the Western Air Quality Study (WAQS)
  WAQS 2011 modeling platform: WRF/SMOKE/CAMx
  Adjustments to the meteorology and modeling domains to optimize for southern New Mexico
Modeling 2011 New Mexico ozone season: May 1 – August 31
Modeling Plan
  Prepare base year emission inventories
  Run WRF/SMOKE/CAMx for 2011 base year
    Evaluate 2011 base year model against observations, refine model if needed
  Prepare future year emission inventories for 2025
  Run SMOKE/CAMx for future year
    Modeled Attainment Test
    Emissions sensitivity/control runs
    Source apportionment to diagnose causes of high ozone in Doña Ana County
  Reporting

## Slide 4: SNMOS Tasks
Completed
  Task 1: 2011 WRF 36/12/4 km with 4 km focus on Dona Ana/El Paso/Juarez and Work Plan (11/30/15)
  Task 2: 2011 update Permian Basin O&G (11/30/15)
  Task 3: 2011 update of Juarez and nearby Mexico EI, 2020 Mexico emissions update (11/30/15)
  Task 4: SMOKE current 2011 NEI for 4 km domain (2/29/16)
  Task 5: Gridded 2011 biogenic, fires, wind-blown dust, lightning emissions for 4 km domain (2/29/16)
  Task 6: Develop 2011 4 km CAMx database and perform base case (2/29/16)
  Task 7: 2011 MPE and sensitivity modeling for Dona Ana County (4/30/16)
  Task 8: SMOKE current FY US EI and FY Mexico emissions update (4/30/16)
  Task 9: FY 12/4-km CAMx simulation (5/31/16)
  Task 10: FY ozone projections (MATS) (5/31/16)
  Task 11: 2025 emissions sensitivity/controls (8/15/16)
This Deliverable Period (9/15/2016)
  Task 12: Ozone source apportionment modeling of 2011 and 2025
Pending
  Task 13: Air Quality Technical Support Document (AQTSD)

## Slide 5: Task 12: Objectives and Deliverables
Objective
  Carry out SNMOS ozone source apportionment CAMx modeling of 2011 and 2025 (Completed July 18, 2016)
Deliverables
  PowerPoint presentation on ozone source apportionment modeling (Completed September 8, 2016)
Tasks
  Run CAMx 12/4 km using ozone source apportionment for 2011 and 2025
  Use EPA’s MATS to calculate design values for both years
    Determine the source regions and source categories that contribute to elevated ozone concentrations in Doña Ana County and vicinity
    Obtain the contributions of Mexico emissions to 2011 ozone Design Values (DVs)
    Calculate 2025 ozone DVs without the contributions of fire emissions
  Prepare PowerPoint Presentation (this document)
  Provide interactive spreadsheet source apportionment results on ozone DVs
  Provide SA Visualization Tool for 2011 and 2025 ozone contributions to MDA8 ozone at monitors (hosted on IWDW and available through wiki)

## Slide 6: CAMx Air Quality Modeling
CAMx configured as in SNMOS Base11b
  See SNMOS Task 7 MPE report
CAMx run for April–August, 2011 and 2025
  2011 dates for 2025 run
Emissions
  Primarily from EPA NEI2011 v6.2 modeling platform 2025 projection
  2020 WAQS oil and gas projections
  Biogenic, lightning, fires, and sea salt constant at 2011 levels
  SNMOS Task 3 deliverable for Mexico future year EI details
  SNMOS Task 8 deliverable for US future year EI details
CAMx OSAT tool used for source apportionment modeling of 2011 and 2025
  Presenting results from 4 km grid

## Slide 7: MATS Configuration
DVF calculation uses maximum concentration from a matrix of modeled grid cells surrounding a monitor
  Current EPA guidance followed here: 3x3 matrix (9 cells)
RRF calculation
  Used top 10 modeled days
  70 ppb threshold
  Minimum number of days at or above threshold: 1 day
To calculate contribution of each source group
  Ran MATS with full CAMx output
  Subtracted ozone contribution from source group X from full model output
  Reran MATS without contribution from X
  Difference of two MATS runs is contribution from X to the DV
  Slides 51 and 52 have calculation details

## Slide 8: Source Groups
4 source regions
  (1) New Mexico; (2) Texas; (3) Mexico; and (4) Arizona with remainder of other states in the 12 km domain
8 emissions source categories
  Natural (biogenics and lighting NOx)
  On-Road Mobile
  Non-Road Mobile
  Oil and Gas (point and non-point)
  Electrical Generating Unit (EGU) Point
  Non-EGU Point
  Open Land Fires (wildfire, prescribed, and agricultural burning)
  Remainder Anthropogenic (mainly area)
Initial and boundary conditions
34 total Source Groups (34 = 4 x 8 + 2)

## Slide 9: Boundary Conditions (BCs)
BCs represent transport from outside of the 12/4 km SNMOS domain:
  Transport from sources in remainder of U.S.
  International transport
  Natural global ozone background including stratospheric intrusions
Includes more than just U.S. background (USB) or North American background (NAB)

## Slide 10: Natural Emissions: Biogenic Isoprene Emissions: 4 km Grid
Large contribution from Mexico natural emissions
Discontinuity at US-Mexico border (white arrow) suggests uncertainty in biogenic emission inventory
MEGAN v2.10 Episode Average Isoprene
Emissions on 4 km Grid
Google Earth Imagery
Of 4 km Domain Region

## Slide 11: Natural Emissions: Lightning NOx July 27-28, 2011
LNOx emissions are uncertain and may affect the contribution from Mexico natural emissions
WRF MSKF NAM Run Precipitation
Column-Integrated LNOx Emissions

## Slide 12: SNMOS 2025 Emissions Modeling
Dona Ana
  Decreases in onroad and offroad mobile NOx emissions
Mexico
  Decreases in onroad mobile NOx
  Increases in EGU and non-EGU point NOx emissions
West Texas
  Decreases in onroad and offroad mobile
  Increases in O&G
Percent Difference ([2025-2011]/2011)
New Mexico
Mexico
W. Texas
Sonora
Notes: Reductions in onroad mobile in all regions, reductions in offroad in US, increases in EGU and non-EGU point emissions in Mexico, increases in O&G emissions in TX and NM

## Slide 13: SNMOS 2025 Emissions Modeling New Mexico 2011 and 2025 NOx Emissions Differences
Absolute Difference (2025-2011)
2025-2011 NOx Emissions

## Slide 14: Which Source Groups Contribute to Doña Ana County Ozone?
How important is transport in determining ozone at Doña Ana monitors?
  Boundary conditions, transport within 12/4 km domain
What emissions source categories contribute at Doña Ana monitors?
  Top contributing source groups at each monitor
  Contribution of New Mexico anthropogenic emissions
  Evaluate consistency of OSAT results with UNC 2011/2025 emissions plots
Detailed results for Desert View and Santa Teresa monitors
  Results for other monitors follow End slide

## Slide 15: Role of Transport Ozone DV at Desert View Monitor
12 km BC contribution to DVs is far larger than those of regions within the 12 km domain
BCs contain effect of
  Sources within the US (e.g. Los Angeles and Phoenix)
  Sources outside the US (Asia, regions of Mexico outside the 12/4 km grid)
  Stratosphere contribution
Similar results for other Doña Ana monitors
Contribution to DV (ppb)
Transport
NM

## Slide 16: Desert View DVC: 71.0 ppb DVF: 65.1 ppb
NM contribution smaller than Texas and Mexico contributions
Reduction in 2025 DV driven by decrease in BCs and in contributions from New Mexico, Texas and Other 12 km
Contribution from Mexico increases slightly

## Slide 17: Desert View DVC: 71.0 ppb DVF: 65.1 ppb
Reductions in Texas, New Mexico and Mexico on-road contributions are responsible for much of ozone decrease in Desert View DV in 2025
Largest 2011 contributions to Desert View DV are from Texas and Mexico on-road and Mexico EGU and natural emissions
Largest 2025 contributions are from Mexico EGU and non-EGU point sources and on-road emissions from Texas and Mexico

## Slide 18: Santa Teresa DVC: 70.3 ppb DVF: 63.8 ppb
Reduction in DV driven by reductions in BCs and contributions from Texas and New Mexico
Contribution from Other 12 km declines
Slight decrease in Mexico contribution

## Slide 19: Santa Teresa DVC: 70.3 ppb DVF: 63.8 ppb
Large reduction in onroad mobile contribution in 2025
Increases in Mexico EGU and Texas oil and gas contributions in 2025
Largest 2011 contributions from Texas, New Mexico and Mexico on-road emissions and Mexico EGUs

## Slide 20: Most Frequent Top 5 Contributors to the DVs of the 6 Doña Ana Monitors
On-road, natural (Mexico) and EGU emissions appear most frequently in the list of top 5 contributors to Doña Ana County monitor DVs
  All 6 Doña Ana County monitors have TX onroad mobile sources in top 5 in 2011
Mexico is the most frequently appearing source region
# of Times Source Group Appears in
List of Top 5 Contributing Sources
Source Group
Notes: Picked top 5 source groups because after 5 source groups, 2011 ozone contribution was often < 1 ppb
Green arrow to call out reduction in frequency of appearance of NM onroad mobile from 2011 to 2025

## Slide 21: Monitors in the 4 km Domain
Hurley
Deming
Carlsbad
Solano
Chaparral
La Union
Desert View
Santa Teresa
Sunland Park
UTEP
Chamizal
Ascarate Park
Socorro Hueco
Ivanhoe
Skyline Park
No Data
No Data

## Slide 22: Contribution of Anthropogenic Emissions from Mexico to DVs for Monitors in 4 km Grid
Contributions to DV from Mexico anthropogenic emissions range from ~2-6 ppb at Doña Ana monitors and are similar in 2011 and 2025
Monitors in NM near US-Mexico border and El Paso monitors have larger contributions from Mexico anthropogenic emissions
Doña Ana

## Slide 23: Contribution of Onroad Mobile Emissions to DVs for Monitors in 4 km Grid
Large 2011 contributions from on-road emissions to DVs at Doña Ana and El Paso monitors
Large decreases in onroad mobile contribution in 2025 for all sites

## Slide 24: Contribution of NM Anthropogenic Emissions to 4 km Grid NM Monitor DVs
Onroad mobile emissions make largest NM anthropogenic contribution to DV at most NM monitors
  Solano monitor has largest contribution from onroad mobile
  Decreases in 2025
Nonroad and O&G make next largest contributions, followed by EGU points
Oil and gas dominates at Carlsbad
  Influence of Permian Basin
  Impact increases in 2025 consistent with projected growth in emissions

## Slide 25: Which Source Groups Contribute to Doña Ana County Ozone?
Boundary conditions are by far the largest contributor
  Typical result for a regional modeling grid
NM contribution smaller than either TX and MEX contribution to DVs for all Doña Ana monitors except Solano
  Solano has a large onroad mobile contribution
In 2011, emissions source categories contributing most to DVs were onroad mobile (TX, NM, MEX), natural emissions (MEX) and EGUs (MEX)
  Onroad mobile contribution is smaller in 2025

## Slide 26: Contribution of Emissions from Mexico to Doña Ana County Ozone
Assess contribution of Mexico emissions to DVs at Dona Ana monitors in 2011 and 2025
  Compare with results of Task 11 Sensitivity Testing
Section 179B “But for” test

## Slide 27: Ozone Contribution to 2011 DVs from Mexico Anthropogenic Emissions
But for the contribution of emissions from Mexico, the Desert View monitor would have attained the 70 ppb NAAQS in 2011
Monitors closer to US-Mexico border have larger Mexico contribution (e.g. El Paso monitors)

## Slide 28: Comparison of Sensitivity Test and Source Apportionment Results
Results are comparable in magnitude and are consistent in showing that Mexico emissions had a significant impact on Doña Ana County DV in 2011
Source apportionment results show similar maximum and average impacts than sensitivity test and lower minimum impact
Contribution of Mexico Emissions to 2011 DVs for Doña Ana County Monitors (4 km Grid Results)

## Slide 29: Contribution of Emissions from Mexico to Doña Ana County Ozone: Summary
But for the contribution of emissions from Mexico, the Desert View monitor would have attained the 70 ppb NAAQS in 2011
  Also true for UTEP monitor in El Paso
Mexico SA contribution to Doña Ana monitor 2011 DVs ranges from 2.5 – 6.3 ppb with average of 4.9 ppb
Monitors closer to US-Mexico border have larger Mexico contribution (e.g. El Paso monitors)
Results of sensitivity test (Task 11) and source apportionment modeling (Task 12) are consistent

## Slide 30: Contribution of Fire Emissions to Doña Ana County Ozone
CAMx modeling of 2011 showed large impacts from fire emissions
  Active fire season during 2011 with large fires within 12 km domain
Treated fires separately from the rest of the natural emission inventory so their impacts could be tracked
Used source apportionment to quantify effect of fire emissions on Doña Ana DVs

## Slide 31: Fire Ozone Impact Example
Wallow Fire plume has modeled 1-hour ozone values > 160 ppb
Model overestimates ground level ozone impacts
PMDETAIL PM2.5 Daily Total Fire Emissions
Wallow Fire
Horseshoe 2 Fire
CAMx 1-hour Average Ozone: June 5, 0Z
Fire
Fire
Fire
Carbon 2 EGU

## Slide 32: Impact of Fire Emissions on 4 km Grid Monitor DV Results: 2025
Impact of fire emissions on 4 km grid monitor 2025 DVFs is small (< |0.5| ppb)
  Used MATS Unmonitored Area Analysis (UAA) to view results across modeling domain

## Slide 33: Impact of Fire Emissions on DV Results: 2011 Unmonitored Area Analysis
2011 DVs With Fires
2011 DVs Without Fires

## Slide 34: Impact of Fire Emissions on DV Results: 2011 Unmonitored Area Analysis
Impact of fire emissions is ≤ |0.5| ppb at Doña Ana County monitors
  Does not affect 2011 DV results
Larger fire impacts on DVs (> 5 ppb) occur elsewhere in 4 km domain downwind of 2011 fires

## Slide 35: Impact of Fire Emissions on DV Results: 2025 Unmonitored Area Analysis
2025 DVs With Fires
2025 DVs Without Fires

## Slide 36: Impact of Fire Emissions on DV Results: 2025 Unmonitored Area Analysis
Impact of fire emissions is ≤ |0.5| ppb at Doña Ana County monitors
  Does not affect 2025 DVF results
Larger fire impacts on DVs (> 5 ppb) occur elsewhere in 4 km domain downwind of 2011 fires

## Slide 37: Contribution of Fire Emissions to Doña Ana County Ozone: Summary
Fire emissions affected 2011 and 2025 DVs at grid cells within the 4 km domain
  UAA shows DV impacts > 5 ppb downwind of the fire locations
Fire emissions had a small (≤ |0.5| ppb) effect on 2011 and 2025 DVs at Doña Ana County monitors
  Impacts too small to affect attainment status results for 2011 and 2025
  Small impacts due to location of monitors relative to 2011 fires

## Slide 38: SA Vis Tools Overview
Modeling results loaded into a web-based Source Apportionment Visualization Tool
Displays base (2011) and future (2025) year MDA8 SA results
  By monitor, by date
  Information on model performance
Documentation in SNMOS wiki on IWDW website

## Slide 39: SA Vis Tools: Results by Region
Results for Sunland Park monitor, 2011

## Slide 40: SA Vis Tools: Source Breakdown by Region

## Slide 41: SA Vis Tools: Results by Emissions Sector

## Slide 42: SA Vis Tools: Regional Breakdown by Emissions Source

## Slide 43: Access SNMOS Ozone SA Vis Tool wiki through IWDW Website (in development)
http://views.cira.colostate.edu/tsdw/

## Slide 44: Task 12 Summary
Transported ozone contributes far more to Doña Ana monitor DVs than New Mexico emissions in 2011 and 2025
  Boundary conditions are the largest contributor, then Mexico and Texas
  Mexico contribution to Doña Ana monitor 2011 DVs ranges from 2.5 – 6.3 ppb with average of 4.9 ppb
OSAT results indicate but for the contribution of anthropogenic emissions from Mexico, the Desert View monitor would have attained the 70 ppb NAAQS in 2011
In 2011 and 2025, emissions source categories contributing most to Doña Ana monitor DVs were onroad mobile (TX, NM, MEX), natural emissions (MEX) and EGUs (MEX)
  Onroad mobile contribution is much (~50%) lower in 2025
Of all New Mexico anthropogenic emissions sources, onroad mobile emissions make largest contribution to DVs at all Doña Ana monitors
  Decreases in 2025
  Nonroad and O&G make next largest contributions, followed by EGU points
Impact of fire emissions on Doña Ana DV analysis is small

## Slide 45: Task 13: Air Quality Technical Support Document
Prepare Air Quality Technical Support Document (TSD)
  TSD will summarize methods and finding of all tasks of the SNMOS
Steps
  Prepare draft TSD documenting Tasks 1-12
  Submit draft TSD for review
  Update draft TSD to reflect comments received and prepare a Response to Comments (RtC) document.
  Submit final TSD

## Slide 46: Air Quality Technical Support Document Outline
Executive Summary
Introduction
SNMOS Task Summaries
  Task 1-13
    Task Summary
    Significant Findings
    Milestones and Deliverables
References

## Slide 47: Task 13: Air Quality Technical Support Document
Current (September 8, 2016) Status:
  All project technical work has been completed
  Currently writing technical support document:
    Outline completed
    Deliverables:
      Sep 30 Draft Technical Support Document (TSD)
      Oct 14 Comments from NMED
      Oct 28 Final TSD
        Response to Comments (RtC) document for NMED
        Modeling data, RtC document, and final TSD also posted on WAQS data warehouse.

## Slide 48: Next Steps Tasks to be Completed by November 18, 2016
Task 1: 2011 WRF 36/12/4 km with 4 km focus on Dona Ana/El Paso/Juarez and Work Plan (Completed)
Task 2: 2011 update Permian Basin O&G (Completed)
Task 3: 2011 update of Juarez and nearby Mexico EI, 2020 Mexico emissions update (Completed)
Task 4: SMOKE current 2011 NEI for 4 km domain (2/29/16)
Task 5: Gridded 2011 biogenic, fires, wind-blown dust, lightning emissions for 4 km domain (2/29/16)
Task 6: Develop 2011 4 km CAMx database and perform base case (2/29/16)
Task 7: 2011 MPE and sensitivity modeling for Dona Ana County (4/30/16)
Task 8: SMOKE current FY US EI and FY Mexico emissions update (4/30/16)
Task 9: FY 4 km CAMx simulation (5/31/16)
Task 10: FY ozone projections (MATS) (5/31/16)
Task 11: FY emissions sensitivity/controls (8/11/16)
Task 12: FY 4 km source apportionment run (9/15/16)
Task 13: Air Quality Technical Support Document (10/28/16)

## Slide 49: End—Questions?

## Slide 50: Biogenic Emissions: 12 km Grid
MEGAN v2.10 Episode Average Isoprene
Emissions on 12 km Grid
MEGAN v2.10 Episode Average Monoterpene
Emissions on 12 km Grid

## Slide 51: Sunland Park DVC: 66.7 ppb DVF: 61.3 ppb
Reduction in DV driven by reductions in BCs and contributions from Texas and New Mexico
Contribution from Other 12 km declines
Slight decrease in Mexico contribution

## Slide 52: Sunland Park DVC: 66.7 ppb DVF: 61.3 ppb
Largest 2011 contributions from Texas and Mexico on-road emissions
Increase in Mexico EGU contribution in 2025

## Slide 53: Solano DVC: 64.3 ppb DVF: 58.7 ppb
Reduction in DV driven by reductions in BCs and contributions from Texas and New Mexico
Contribution from Other 12 km declines
Slight decrease in Mexico contribution

## Slide 54: Solano DVC: 64.3 ppb DVF: 58.7 ppb
Largest 2011 contributions from Texas and Mexico on-road emissions
Increase in Mexico EGU contribution in 2025

## Slide 55: La Union DVC: 64.7 ppb DVF: 58.3 ppb
Reduction in DV driven by reductions in BCs and contributions from Texas and New Mexico
Contribution from Other 12 km declines
Slight decrease in Mexico contribution

## Slide 56: La Union DVC: 64.7 ppb DVF: 58.3 ppb
Largest 2011 contributions from Texas and Mexico on-road emissions
Increase in Mexico EGU contribution in 2025

## Slide 57: Chaparral DVC: 67.7 ppb DVF: 60.8 ppb
Reduction in DV driven by reductions in BCs and contributions from Texas and New Mexico
Contribution from Other 12 km declines
Slight decrease in Mexico contribution

## Slide 58: Chaparral DVC: 67.7 ppb DVF: 60.8 ppb
Largest 2011 contributions from Texas and Mexico on-road emissions
Increase in Mexico EGU contribution in 2025

## Slide 59: Top 5 Contributors to 4 km Grid Non-Doña Ana New Mexico Monitor DVs
Largest 2011 contributions from Texas and Mexico on-road emissions
Increase in Mexico EGU contribution in 2025
Notes: Hurley, Carlsbad, Deming

## Slide 60: Ozone Contribution Calculations: 2025

## Slide 61: Ozone Contribution Calculations: 2011